## Slide 1: Memory Systems Fundamentals, Recent Research, Challenges, Opportunities Lecture 6: Memory Interference and QoS
Prof. Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
10 October 2018
Technion Fast Course 2018

## Slide 2: Shared Resource Design for Multi-Core Systems

## Slide 3: Memory System: A Shared Resource View
Storage
Most of the system is dedicated to storing and moving data

## Slide 4: Resource Sharing Concept
Idea: Instead of dedicating a hardware resource to a hardware context, allow multiple contexts to use it
  Example resources: functional units, pipeline, caches, buses, memory, interconnects, storage
Why?
+ Resource sharing improves utilization/efficiency  throughput
  When a resource is left idle by one thread, another thread can use it; no need to replicate shared data
+ Reduces communication latency
  For example, shared data kept in the same cache in SMT processors
+ Compatible with the shared memory model

## Slide 5: Resource Sharing Disadvantages
Resource sharing results in contention for resources
  When the resource is not idle, another thread cannot use it
  If space is occupied by one thread, another thread needs to re-occupy it
- Sometimes reduces each or some thread’s performance
- Thread performance can be worse than when it is run alone
- Eliminates performance isolation  inconsistent performance across runs
- Thread performance depends on co-executing threads
- Uncontrolled (free-for-all) sharing degrades QoS
- Causes unfairness, starvation
Need to efficiently and fairly utilize shared resources

## Slide 6: Resource Sharing vs. Partitioning
Sharing improves throughput
  Better utilization of space
Partitioning provides performance isolation (predictable performance)
  Dedicated space
Can we get the benefits of both?
Idea: Design shared resources such that they are efficiently utilized, controllable and partitionable
  No wasted resource + QoS mechanisms for threads

## Slide 7: Memory System is the Major Shared Resource
threads’ requests
interfere

## Slide 8: Much More of a Shared Resource in Future

## Slide 9: Inter-Thread/Application Interference
Problem: Threads share the memory system, but memory system does not distinguish between threads’ requests
Existing memory systems
  Free-for-all, shared based on demand
  Control algorithms thread-unaware and thread-unfair
  Aggressive threads can deny service to others
  Do not try to reduce or control inter-thread interference

## Slide 10: Unfair Slowdowns due to Interference
(Core 0)
(Core 1)
Moscibroda and Mutlu, “Memory performance attacks: Denial of memory service
in multi-core systems,” USENIX Security 2007.
matlab
(Core 1)
gcc
(Core 2)
Notes: What kind of performance do we expect when we run two applications on a multi-core system? To answer this question, we performed an experiment. We took two applications we cared about, ran them together on different cores in a dual-core system, and measured their slowdown compared to when each is run alone on the same system. This graph shows the slowdown each app experienced. (DATA explanation…)
Why do we get such a large disparity in the slowdowns?
Is it the priorities? No. We went back and gave high priority to gcc and low priority to matlab. The slowdowns did not change at all. Neither the software or the hardware enforced the priorities.
Is it the contention in the disk? We checked for this possibility, but found that these applications did not have any disk accesses in the steady state. They both fit in the physical memory and therefore did not interfere in the disk.
What is it then? Why do we get such large disparity in slowdowns in a dual core system?
I will call such an application a “memory performance hog”
Now, let me tell you why this disparity in slowdowns happens.
Is it that there are other applications or the OS interfering with gcc, stealing its time quantums? No.

## Slide 11: Uncontrolled Interference: An Example
CORE 1
CORE 2
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
DRAM
Bank 0
DRAM
Bank 1
DRAM
Bank 2
Shared DRAM
Memory System
Multi-Core
Chip
unfairness
INTERCONNECT
stream
random
DRAM
Bank 3
Notes: -In a multi-core chip, different cores share some hardware resources. In particular, they share the DRAM memory system. The shared memory system consists of this and that.
When we run matlab on one core, and gcc on another core, both cores generate memory requests to access the DRAM banks. When these requests arrive at the DRAM controller, the controller favors matlab’s requests over gcc’s requests. As a result, matlab can make progress and continues generating memory requests. These requests are again favored by the DRAM controller over gcc’s requests. Therefore, gcc starves waiting for its requests to be serviced in DRAM whereas matlab makes very quick progress as if it were running alone.
Why does this happen? This is because the algorithms employed by the DRAM controller are unfair.
But, why are these algorithms unfair? Why do they unfairly prioritize matlab accesses?
To understand this, we need to understand how a DRAM bank operates.
Almost all systems today contain multi-core chips
Multi-core systems consist of multiple on-chip cores and caches
Cores share the DRAM memory system
DRAM memory system consists of
  DRAM banks that store data (multiple banks to allow parallel accesses)
  DRAM memory controller that mediates between cores and DRAM memory
    It schedules memory operations generated by cores to DRAM
This talk is about exploiting the unfair algorithms in the memory controllers to perform denial of service to running threads
To understand how this happens, we need to know about how each DRAM bank operates

## Slide 12: A Memory Performance Hog
// initialize large arrays A, B
for (j=0; j<N; j++) {
index = rand();
A[index] = B[index];
…
}
STREAM
Sequential memory access
Very high row buffer locality (96% hit rate)
Memory intensive
RANDOM
Random memory access
Very low row buffer locality (3% hit rate)
Similarly memory intensive
// initialize large arrays A, B
for (j=0; j<N; j++) {
index = j*linesize;
A[index] = B[index];
…
}
streaming
random
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.
Notes: Streaming through memory by performing operations on two 1D arrays.
Sequential memory access
Each access is a cache miss (elements of array larger than a cache line size)  hence, very memory intensive
Link to the real code…

## Slide 13: What Does the Memory Hog Do?
Row Buffer
Row decoder
Column mux
Data
Row 0
T0: Row 0
Row 0
T1: Row 16
T0: Row 0
T1: Row 111
T0: Row 0
T0: Row 0
T1: Row 5
T0: Row 0
T0: Row 0
T0: Row 0
T0: Row 0
T0: Row 0
Memory Request Buffer
T0: STREAM
T1: RANDOM
Row size: 8KB, cache block size: 64B
128 (8KB/64B) requests of T0 serviced before T1
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.
Notes: Pictorially demonstrate how stream denies memory service to rdarray
Stream continuously accesses columns in row 0 in a streaming manner (streams through a row after opening it)
In other words almost all its requests are row-hits
RDarray’s requests are row-conflicts (no locality)
The DRAM controller reorders streams requests to the open row over other requests (even older ones) to maximize DRAM throughput
Hence, rdarray’s requests do not get serviced as long as stream is issuing requests at a fast-enough rate
In this example, the red thread’s request to another row will not get serviced until stream stops issuing a request to row 0
With those parameters, 128 requests of stream would be serviced before 1 from rdarray
As row-buffer size increases, which is the industry trend, this problem will become more severe
This is not the worst case, but it is easy to construct and understand
  Stream falls off the row buffer at some point
I leave it to the listeners to construct a case worse than this (it is possible)

## Slide 14: DRAM Controllers
A row-conflict memory access takes significantly longer than a row-hit access
Current controllers take advantage of the row buffer
Commonly used scheduling policy (FR-FCFS) [Rixner 2000]*
  (1) Row-hit first: Service row-hit memory accesses first
  (2) Oldest-first: Then service older accesses first
This scheduling policy aims to maximize DRAM throughput
    But, it is unfair when multiple threads share the DRAM system
*Rixner et al., “Memory Access Scheduling,” ISCA 2000.
*Zuravleff and Robinson, “Controller for a synchronous DRAM …,” US Patent 5,630,096, May 1997.

## Slide 15: Effect of the Memory Performance Hog
Chart: 
| STREAM | RANDOM
Column1 | 1.18 | 2.82
1.18X slowdown
2.82X slowdown
Results on Intel Pentium D running Windows XP
(Similar results for Intel Core Duo and AMD Turion, and on Fedora Linux)
Slowdown
Chart: 
| STREAM | gcc
Column1 | 1.23 | 2.91
Chart: 
| STREAM | Virtual PC
Column1 | 1.21 | 2.59
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.
Notes: RANDOM was given higher OS priority in the experiments

## Slide 16: Greater Problem with More Cores
Vulnerable to denial of service (DoS)
Unable to enforce priorities or SLAs
Low system performance
Uncontrollable, unpredictable system

## Slide 17: Greater Problem with More Cores
Vulnerable to denial of service (DoS)
Unable to enforce priorities or SLAs
Low system performance
Uncontrollable, unpredictable system

## Slide 18: Distributed DoS in Networked Multi-Core Systems
Attackers
(Cores 1-8)
Stock option pricing application
(Cores 9-64)
Cores connected via
packet-switched
routers on chip
~5000X latency increase
Grot, Hestness, Keckler, Mutlu,
“Preemptive virtual clock: A Flexible,
Efficient, and Cost-effective QOS
Scheme for Networks-on-Chip,“
MICRO 2009.

## Slide 19: More on Memory Performance Attacks
Thomas Moscibroda and Onur Mutlu, "Memory Performance Attacks: Denial of Memory Service in Multi-Core Systems" Proceedings of the 16th USENIX Security Symposium (USENIX SECURITY), pages 257-274, Boston, MA, August 2007. Slides (ppt)

## Slide 20: More on Interconnect Based Starvation
Boris Grot, Stephen W. Keckler, and Onur Mutlu, "Preemptive Virtual Clock: A Flexible, Efficient, and Cost-effective QOS Scheme for Networks-on-Chip" Proceedings of the 42nd International Symposium on Microarchitecture (MICRO), pages 268-279, New York, NY, December 2009. Slides (pdf)

## Slide 21: How Do We Solve The Problem?
Inter-thread interference is uncontrolled in all memory resources
  Memory controller
  Interconnect
  Caches
We need to control it
  i.e., design an interference-aware (QoS-aware) memory system

## Slide 22: QoS-Aware Memory Systems: Challenges
How do we reduce inter-thread interference?
  Improve system performance and core utilization
  Reduce request serialization and core starvation
How do we control inter-thread interference?
  Provide mechanisms to enable system software to enforce QoS policies
  While providing high system performance
How do we make the memory system configurable/flexible?
  Enable flexible mechanisms that can achieve many goals
    Provide fairness or throughput when needed
    Satisfy performance guarantees when needed

## Slide 23: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers
  QoS-aware interconnects
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system
  QoS-aware data mapping to memory controllers
  QoS-aware thread scheduling to cores

## Slide 24: Fundamental Interference Control Techniques
Goal: to reduce/control inter-thread memory interference
1. Prioritization or request scheduling
2. Data mapping to banks/channels/ranks
3. Core/source throttling
4. Application/thread scheduling

## Slide 25: QoS-Aware Memory Scheduling
How to schedule requests to provide
  High system performance
  High fairness to applications
  Configurability to system software
Memory controller needs to be aware of threads
Memory Controller
Core
Core
Core
Core
Memory
Resolves memory contention by scheduling requests

## Slide 26: QoS-Aware Memory Scheduling: Evolution

## Slide 27: QoS-Aware Memory Scheduling: Evolution
Stall-time fair memory scheduling [Mutlu+ MICRO’07]
  Idea: Estimate and balance thread slowdowns
  Takeaway: Proportional thread progress improves performance, especially when threads are “heavy” (memory intensive)
Parallelism-aware batch scheduling [Mutlu+ ISCA’08, Top Picks’09]
  Idea: Rank threads and service in rank order (to preserve bank parallelism); batch requests to prevent starvation
  Takeaway: Preserving within-thread bank-parallelism improves performance; request batching improves fairness
ATLAS memory scheduler [Kim+ HPCA’10]
  Idea: Prioritize threads that have attained the least service from the memory scheduler
  Takeaway: Prioritizing “light” threads improves performance

## Slide 28: QoS-Aware Memory Scheduling: Evolution
Thread cluster memory scheduling [Kim+ MICRO’10, Top Picks’11]
  Idea: Cluster threads into two groups (latency vs. bandwidth sensitive); prioritize the latency-sensitive ones; employ a fairness policy in the bandwidth sensitive group
  Takeaway: Heterogeneous scheduling policy that is different based on thread behavior maximizes both performance and fairness
Integrated Memory Channel Partitioning and Scheduling [Muralidhara+ MICRO’11]
    Idea: Only prioritize very latency-sensitive threads in the scheduler; mitigate all other applications’ interference via channel partitioning
    Takeaway: Intelligently combining application-aware channel partitioning and memory scheduling provides better performance than either

## Slide 29: QoS-Aware Memory Scheduling: Evolution
Parallel application memory scheduling [Ebrahimi+ MICRO’11]
  Idea: Identify and prioritize limiter threads of a multithreaded application in the memory scheduler; provide fast and fair progress to non-limiter threads
  Takeaway: Carefully prioritizing between limiter and non-limiter threads of a parallel application improves performance
Staged memory scheduling [Ausavarungnirun+ ISCA’12]
    Idea: Divide the functional tasks of an application-aware memory scheduler into multiple distinct stages, where each stage is significantly simpler than a monolithic scheduler
    Takeaway: Staging enables the design of a scalable and relatively simpler application-aware memory scheduler that works on very large request buffers

## Slide 30: QoS-Aware Memory Scheduling: Evolution
MISE: Memory Slowdown Model [Subramanian+ HPCA’13]
    Idea: Estimate the performance of a thread by estimating its change in memory request service rate when run alone vs. shared  use this simple model to estimate slowdown to design a scheduling policy that provides predictable performance or fairness
    Takeaway: Request service rate of a thread is a good proxy for its performance; alone request service rate can be estimated by giving high priority to the thread in memory scheduling for a while
ASM: Application Slowdown Model [Subramanian+ MICRO’15]
  Idea: Extend MISE to take into account cache+memory interference
  Takeaway: Cache access rate of an application can be estimated accurately and is a good proxy for application performance

## Slide 31: QoS-Aware Memory Scheduling: Evolution
BLISS: Blacklisting Memory Scheduler [Subramanian+ ICCD’14, TPDS’16]
  Idea: Deprioritize (i.e., blacklist) a thread that has consecutively serviced a large number of requests
  Takeaway: Blacklisting greatly reduces interference enables the scheduler to be simple without requiring full thread ranking
DASH: Deadline-Aware Memory Scheduler [Usui+ TACO’16]
  Idea: Balance prioritization between CPUs, GPUs and Hardware Accelerators (HWA) by keeping HWA progress in check vs. deadlines such that HWAs do not hog performance and appropriately distinguishing between latency-sensitive vs. bandwidth-sensitive CPU workloads
  Takeaway: Proper control of HWA progress and application-aware CPU prioritization leads to better system performance while meeting HWA deadlines

## Slide 32: QoS-Aware Memory Scheduling: Evolution
Prefetch-aware shared resource management [Ebrahimi+ ISCA’11] [Ebrahimi+ MICRO’09] [Ebrahimi+ HPCA’09] [Lee+ MICRO’08’09]
  Idea: Prioritize prefetches depending on how they affect system performance; even accurate prefetches can degrade performance of the system
  Takeaway: Carefully controlling and prioritizing prefetch requests improves performance and fairness
DRAM-Aware last-level cache policies and write scheduling [Lee+ HPS Tech Report’10] [Seshadri+ ISCA’14]
  Idea: Design cache eviction and replacement policies such that they proactively exploit the state of the memory controller and DRAM (e.g., proactively evict data from the cache that hit in open rows)
  Takeaway: Coordination of last-level cache and DRAM policies improves performance and fairness; writes should not be ignored

## Slide 33: QoS-Aware Memory Scheduling: Evolution
FIRM: Memory Scheduling for NVM [Zhao+ MICRO’14]
  Idea: Carefully handle write-read prioritization with coarse-grained batching and application-aware scheduling
  Takeaway: Carefully controlling and prioritizing write requests improves performance and fairness; write requests are especially critical in NVMs
Criticality-Aware Memory Scheduling for GPUs [Jog+ SIGMETRICS’16]
  Idea: Prioritize latency-critical cores’ requests in a GPU system
  Takeaway: Need to carefully balance locality and criticality to make sure performance improves by taking advantage of both
Worst-case Execution Time Based Memory Scheduling for Real-Time Systems [Kim+ RTAS’14, JRTS’16]

## Slide 34: Stall-Time Fair Memory Scheduling
Onur Mutlu and Thomas Moscibroda, "Stall-Time Fair Memory Access Scheduling for Chip Multiprocessors" 40th International Symposium on Microarchitecture (MICRO),
pages 146-158, Chicago, IL, December 2007. Slides (ppt)
STFM Micro 2007 Talk

## Slide 35: The Problem: Unfairness
Vulnerable to denial of service (DoS)
Unable to enforce priorities or SLAs
Low system performance
Uncontrollable, unpredictable system

## Slide 36: How Do We Solve the Problem?
Stall-time fair memory scheduling [Mutlu+ MICRO’07]
Goal: Threads sharing main memory should experience similar slowdowns compared to when they are run alone  fair scheduling
    Also improves overall system performance by ensuring cores make “proportional” progress
Idea: Memory controller estimates each thread’s slowdown due to interference and schedules requests in a way to balance the slowdowns
Mutlu and Moscibroda, “Stall-Time Fair Memory Access Scheduling for Chip Multiprocessors,” MICRO 2007.

## Slide 37: Stall-Time Fairness in Shared DRAM Systems
A DRAM system is fair if it equalizes the slowdown of equal-priority threads relative to when each thread is run alone on the same system
DRAM-related stall-time: The time a thread spends waiting for DRAM memory
STshared: DRAM-related stall-time when the thread runs with other threads
STalone: DRAM-related stall-time when the thread runs alone
Memory-slowdown = STshared/STalone
  Relative increase in stall-time
Stall-Time Fair Memory scheduler (STFM) aims to equalize Memory-slowdown for interfering threads, without sacrificing performance
  Considers inherent DRAM performance of each thread
  Aims to allow proportional progress of threads
Notes: Memory-slowdown is the relative increase in the DRAM-related stall-time due to interference from other threads
For example, if a thread’s DRAM related stall time is 1 hour when running alone, and its stall-time is 2 hours when it runs together with other threads,
Its memory-slowdown is said to be 2.
Give an example at the end: If a thread waits for DRAM 1 hour running by itself and this increases to 2 hours (its slowdown is 2), then a thread that waits for DRAM 2 hours, should now wait for DRAM 4 hours.
Each thread experiences the same slowdown compared to its baseline DRAM performance
The amount of time a thread spends waiting for DRAM memory
Extra time a thread requires to run because DRAM access is not instant
PROPORTIONALITY: Each thread makes the same amount of progress relative to its baseline performance. This is consistent with priority based scheduling mechanisms that allocate the same time quantum for equal-priority threads.
We define two values to compute slowdown.
Proportional slowdown (proportionate progress)
  Fairness notion similar to SMT [Cazorla, IEEE Micro’04][Luo, ISPASS’01], SoEMT [Gabor, Micro’06], and shared caches [Kim, PACT’04]

## Slide 38: STFM Scheduling Algorithm [MICRO’07]
For each thread, the DRAM controller
  Tracks STshared
  Estimates STalone
Each cycle, the DRAM controller
  Computes Slowdown = STshared/STalone for threads with legal requests
  Computes unfairness = MAX Slowdown / MIN Slowdown
If unfairness < 
  Use DRAM throughput oriented scheduling policy
If unfairness ≥ 
  Use fairness-oriented scheduling policy
    (1) requests from thread with MAX Slowdown first
    (2) row-hit first , (3) oldest-first
Notes: Except for pathological cases, best achievable unfairness value is 1
Maximizes DRAM throughput if it cannot improve fairness
WORK CONSERVING: Does not waste useful bandwidth to improve fairness
    If a request does not interfere with any other, it is scheduled

## Slide 39: How Does STFM Prevent Unfairness?
Row Buffer
Data
Row 0
T0: Row 0
Row 0
T1: Row 16
T0: Row 0
T1: Row 111
T0: Row 0
T0: Row 0
T1: Row 5
T0: Row 0
T0: Row 0
T0: Row 0
T0 Slowdown
T1 Slowdown
1.00
1.00
1.00
Unfairness
1.03
1.03
1.06
1.06

1.05
1.03
1.06
1.03
1.04
1.08
1.04
1.04
1.11
1.06
1.07
1.04
1.10
1.14
1.03
Row 16
Row 111
Notes: A pictorial example of how our solution prevents stream from being a memory performance hog
Our technique requires the DRAM controller to keep track of slowdowns for each thread and the unfairness value based on these slowdowns
Alpha parameter (maximum tolerable unfairness until the fairness-oriented scheduling policy kicks in) is set to 1.05 in this example
As stream’s requests are prioritized over rdarray’s, rdarray’s slowdown increases and hence unfairness increases
Once unfairness crosses the alpha value, our algorithm kicks in and uses the fairness-oriented scheduling policy
This policy prioritizes requests from the thread with the maximum slowdown (rdarray – thread 1)
Hence, rdarray’s requests do not indefinitely starve
Servicing rdarray’s request increases stream’s slowdown and keeps in check rdarray’s slowdown (thus reduces unfairness)
Therefore, when unfairness becomes tolerable again, our algorithm switches back to the baseline scheduling policy to maximize throughput (i.e. it schedules stream’s row hit requests first, and then the oldest requests)

## Slide 40: STFM Pros and Cons
Upsides:
  First algorithm for fair multi-core memory scheduling
  Provides a mechanism to estimate memory slowdown of a thread
  Good at providing fairness
  Being fair can improve performance
Downsides:
  Does not handle all types of interference
  (Somewhat) complex to implement
  Slowdown estimations can be incorrect

## Slide 41: More on STFM
Onur Mutlu and Thomas Moscibroda, "Stall-Time Fair Memory Access Scheduling for Chip Multiprocessors" Proceedings of the 40th International Symposium on Microarchitecture (MICRO), pages 146-158, Chicago, IL, December 2007. [Summary] [Slides (ppt)]

## Slide 42: Parallelism-Aware Batch Scheduling
Onur Mutlu and Thomas Moscibroda, "Parallelism-Aware Batch Scheduling: Enhancing both
Performance and Fairness of Shared DRAM Systems” 35th International Symposium on Computer Architecture (ISCA),
pages 63-74, Beijing, China, June 2008. Slides (ppt)
PAR-BS ISCA 2008 Talk

## Slide 43: Another Problem due to Memory Interference
Processors try to tolerate the latency of DRAM requests by generating multiple outstanding requests
  Memory-Level Parallelism (MLP)
  Out-of-order execution, non-blocking caches, runahead execution
Effective only if the DRAM controller actually services the multiple requests in parallel in DRAM banks
Multiple threads share the DRAM controller
DRAM controllers are not aware of a thread’s MLP
  Can service each thread’s outstanding requests serially, not in parallel
Notes: Modern processors try to amortize the latency of DRAM requests by generating multiple outstanding requests
This concept is called memory-level parallelism.
Many techniques, such as OOO, non-blocking caches and runahead execution, are designed or used to tolerate long memory latencies by exploiting memory-level parallelism
These latency tolerance techniques are effective only if the DRAM controller actually services the multiple requests of a thread in parallel in DRAM banks
This is true in a single-threaded system since only one thread has exclusive access to all DRAM banks.
However, in a multi-core system, multiple threads share the DRAM controller.
Unfortunately, existing DRAM controllers are not aware of each thread’s memory level parallelism
As a result they can service each thread’s outstanding requests serially, not in parallel
Let’s take a look at why this happens.
-----------------------------------------
Assuming requests are to different banks
In a single core system this is fine because only one thread has exclusive access to all DRAM banks.
However, in a multi-core system, multiple threads shared the DRAM controller.
Unfortunately, DRAM controllers are unaware of a thread’s MLP. As a result, because threads can interfere with each other in the DRAM system, they can service each thread’s requests serially instead of in parallel.
Let’s take a look at why this happens.

## Slide 44: Bank Parallelism of a Thread
Thread A: Bank 0, Row 1
Thread A: Bank 1, Row 1
Bank access latencies of the two requests overlapped
Thread stalls for ~ONE bank access latency
Thread A :
Bank 0
Bank 1
Compute
2 DRAM Requests
Bank 0
Stall
Compute
Bank 1
Single Thread:
Notes: I will demonstrate this pictorially with an example.
Let’s say a thread A executes until it encounters 2 DRAM requests caused by two of its load instructions. These requests are sent to the DRAM controller. And, the controller services them by first scheduling the request to Bank 0 and then scheduling the request to Bank 1. While the requests are being serviced in parallel in the banks, the thread stalls (waiting for the data). Once the servicing of the requests completes, the thread can continue execution.
Since the requests were serviced in parallel in the two banks, bank access latencies of the two requests are overlapped. As a result, the thread stalls for approximately one bank access latency, instead of two bank access latencies.

## Slide 45: Bank Parallelism Interference in DRAM
Compute
Compute
2 DRAM Requests
Bank 0
Bank 1
Thread A: Bank 0, Row 1
Thread B: Bank 1, Row 99
Thread B: Bank 0, Row 99
Thread A: Bank 1, Row 1
A :
Compute
2 DRAM Requests
Bank 0
Stall
Bank 1
Baseline Scheduler:
B:
Compute
Bank 0
Stall
Bank 1
Stall
Stall
Bank access latencies of each thread serialized
Each thread stalls for ~TWO bank access latencies
Notes: What happens when we run two of these threads together in a dual-core system? Again, both threads execute until each encounters 2 DRAM requests. These requests are sent to the DRAM controller. Assume they arrive in the order shown. And the controller services them in the order they arrive.
The controller first takes Thread A’s request to Bank 0 and schedules it. It then schedules Thread B’s request to Bank 1. While these two requests are serviced in parallel, both threads stall.
Once the first request to Bank 0 is done, the controller takes Thread B’s request to bank 0 and schedules it. And it takes Thread A’s request to Bank 1 and schedules it. While these two requests are serviced in parallel, both threads stall.
Once the requests are complete, the threads continue computation.
In this case, because the threads’ requests interfered with each other in the DRAM system, the bank access latencies of each thread were serialized because the requests were serialized. As a result both threads stall for two bank access latencies instead of 1, which is what each thread experienced when running alone.
This is because the DRAM controller did not try to preserve the bank parallelism of each thread.

## Slide 46: Parallelism-Aware Scheduler
2 DRAM Requests
Bank 0
Bank 1
Thread A: Bank 0, Row 1
Thread B: Bank 1, Row 99
Thread B: Bank 0, Row 99
Thread A: Bank 1, Row 1
A :
2 DRAM Requests
Parallelism-aware Scheduler:
B:
Compute
Bank 0
Stall
Compute
Bank 1
Stall
2 DRAM Requests
A :
Compute
2 DRAM Requests
Bank 0
Stall
Compute
Bank 1
B:
Compute
Bank 0
Stall
Compute
Bank 1
Stall
Stall
Baseline Scheduler:
Compute
Bank 0
Stall
Compute
Bank 1
Saved Cycles
Average stall-time: ~1.5 bank access latencies
Notes: Can we do better than this? Let me describe what a parallelism aware scheduler would do.
This is the same example. The two threads compute until they each generate 2 DRAM requests, which arrive at the controller in the same order as before. The controller first takes Thread A’s request to Bank 0 and schedules it. But then, instead of servicing the requests in their arrival order, it realizes there is another request from Thread A to Bank 1 and if it schedules that one back to back with Thread A’s previous request, thread A’s request latencies would be overlapped.
Therefore, the controller takes Thread A’s request to Bank 1 and schedules it. While these two requests are serviced in parallel in the banks, both threads stall.
Once the request to Bank 0 is complete, the controller takes Thread B’s request to Bank 0 and schedules it. Later, it schedules Thread B’s request to Bank 1. While these two requests are being serviced, Thread B stalls (because it does not have the data it needs), but thread A can do useful computation! This is because its requests were serviced in parallel in the banks, instead of serially, and the thread has all the data it needs to do useful computation. As a result, the execution time of Thread A reduces compared to the baseline scheduler that was not aware of the threads’ bank parallelism.
Overall system throughput also improves because the average stall-time of the threads is 1.5 bank access latencies instead of 2. Instead of stalling, cores can make progress executing their instruction streams.

## Slide 47: Parallelism-Aware Batch Scheduling (PAR-BS)
Principle 1: Parallelism-awareness
  Schedule requests from a thread (to different banks) back to back
  Preserves each thread’s bank parallelism
  But, this can cause starvation…
Principle 2: Request Batching
  Group a fixed number of oldest requests from each thread into a “batch”
  Service the batch before all other requests
  Form a new batch when the current one is done
  Eliminates starvation, provides fairness
  Allows parallelism-awareness within a batch
Bank 0
Bank 1
T1
T1
T0
T0
T2
T2
T3
T3
T2
T2
T2
Batch
T0
T1
T1
  Mutlu and Moscibroda, “Parallelism-Aware Batch Scheduling,” ISCA 2008.
Notes: Parallelism aware batch scheduling uses two key principles. The first principle is parallelism awareness. As I showed you before, a thread’s bank parallelism is improved by scheduling requests from a thread to different banks back to back. Unfortunately, doing this greedily can cause starvation because a thread whose requests are continuously scheduled back to back can keep on generating more requests and therefore deny service to other threads that are waiting to access the same bank.
  To avoid this, we use a second principle, called request batching. With this, the controller groups a fixed number of oldest requests from each thread into a “batch”. And, it services the batch before all other requests. It forms a new batch when the current one is done.
  Batching eliminates starvation of requests and threads, and provides fairness. It also allows parallelism of each thread to be optimized for within a batch.
  Let’s take a look at how this works pictorially.
  Multiple threads send requests to the DRAM controller. The controller groups these requests into a batch. Once a batch is formed any newly arriving requests are not included in the batch. Within the batch, the controller schedules each thread’s requests in parallel. It first takes TX’s requests and schedules them in parallel. Then it takes TY’s requests and schedules them in parallel. Note that incoming requests from T3 that are outside the batch are not serviced. Once all requests in the batch are serviced in a parallelism-aware manner, the controller forms a new batch with the requests in the memory request buffer.

## Slide 48: PAR-BS Components
Request batching
Within-batch scheduling
  Parallelism aware
Notes: PAR-BS has two components, which I will describe in more detail. The first is request batching. Aside from guaranteeing starvation freedom and providing fairness, a batch provides a flexible substrate that enables aggressive scheduling optimizations (within the batch).
The second component is the within-batch scheduling component. Within a batch, any DRAM scheduling policy can be employed. And, this policy can be very aggressive and possibly unfair in the global sense. Because the overlying batching scheme ensures forward progress in each thread. In fact, we use a globally unfair shortest job first scheduling policy within a batch, to optimize each thread’s bank parallelism.

## Slide 49: Request Batching
Each memory request has a bit (marked) associated with it
Batch formation:
  Mark up to Marking-Cap oldest requests per bank for each thread
  Marked requests constitute the batch
  Form a new batch when no marked requests are left
Marked requests are prioritized over unmarked ones
  No reordering of requests across batches: no starvation, high fairness
How to prioritize requests within a batch?
Notes: To implement batching, Each memory request has a bit (called the marked bit) associated with it
When a batch is formed, the controller marks up to a Marking-Cap pending requests per bank for each thread. Marked requests constitute the batch. A new batch is formed when no marked requests are left.
  The key idea is that marked requests are always prioritized over unmarked ones. Hence, there is no reordering of requests across batches: As a result, there is no starvation, and a high degree of fairness.
  But how does the controller prioritize requests within a batch?

## Slide 50: Within-Batch Scheduling
Can use any existing DRAM scheduling policy
  FR-FCFS (row-hit first, then oldest-first) exploits row-buffer locality
But, we also want to preserve intra-thread bank parallelism
  Service each thread’s requests back to back
Scheduler computes a ranking of threads when the batch is formed
  Higher-ranked threads are prioritized over lower-ranked ones
  Improves the likelihood that requests from a thread are serviced in parallel by different banks
    Different threads prioritized in the same order across ALL banks
HOW?
Notes: Within a batch, the controller can use any existing DRAM scheduling policy. For example, the baseline FR-FCFS policy is very good at exploiting row buffer locality.
However, in addition to exploiting row-buffer locality, we also want to preserve intra-thread bank parallelism. As I showed you before, this can be accomplished by servicing each thread’s requests back to back
To do so, the DRAM scheduler computes a ranking of threads when the batch is formed
And it prioritizes requests that belong to higher-ranked threads over those that belong to lower ranked ones
  This Improves the likelihood that requests from a thread are serviced in parallel by different banks
  Because Different threads prioritized in the same order (the RANK ORDER) across ALL banks
But how does the scheduler compute this ranking?

## Slide 51: Thread Ranking
Bank 0
Bank 1
req
req
req
req
memory service timeline
thread A
thread B
thread execution timeline
WAIT
WAIT
thread B
thread A
Bank 0
Bank 1
req
req
req
req
memory service timeline
thread execution timeline
WAIT
WAIT
rank
thread B
thread A
thread A
thread B
SAVED CYCLES
Key Idea:
Notes: A memory scheduler can actively exploit bank-level parallelism to reduce the effective memory access latency. Here’s how.
Let us assume a case where two threads send two memory requests to two different banks.
A naïve memory scheduler that doesn’t exploit bank-level parallelism would schedule the requests in the order they arrived.
As shown in their thread execution timeline, both threads must wait for two bank latencies before all their requests are serviced.
In contrast, a memory scheduler that is aware of bank-level parallelism was proposed by Mutlu and Moscibroda.
Their key idea was to rank the threads so that thread’s memory requests are prioritized in the same order across all the banks.
In this case, let us assume that the blue thread’s request are the most prioritized.
The scheduler would then reorder the requests at bank 1’s request buffer…
so that the blue requests are serviced concurrently, after which the red requests can be serviced concurrently.
The memory service timeline shows how the access latencies for requests from the same thread are overlapped.
And, as a result, thread A has to wait less for its requests to be serviced.

## Slide 52: How to Rank Threads within a Batch
Ranking scheme affects system throughput and fairness
Maximize system throughput
  Minimize average stall-time of threads within the batch
Minimize unfairness (Equalize the slowdown of threads)
  Service threads with inherently low stall-time early in the batch
  Insight: delaying memory non-intensive threads results in high slowdown
Shortest stall-time first (shortest job first) ranking
  Provides optimal system throughput [Smith, 1956]*
  Controller estimates each thread’s stall-time within the batch
  Ranks threads with shorter stall-time higher
* W.E. Smith, “Various optimizers for single stage production,” Naval Research Logistics Quarterly, 1956.
Notes: The thread ranking scheme affects system throughput and fairness
A good ranking scheme should achieve two objectives.
First, it should maximize system throughput
Second, it should minimize unfairness; in other words it should balance the slowdown of the threads compared to when each is run alone.
These two objectives call for the same ranking scheme, as I will show soon.
Maximizing system throughput is achieved by minimizing the average stall-time of the threads within the batch (as I showed in the earlier example). By minimizing the average stall time, we maximize the amount of time the system spends on computation rather than waiting for DRAM accesses.
Minimizing unfairness is achieved by servicing threads with inherently low stall-time early in the batch, The insight is that if a thread has low stall time to begin with (if it is not intensive) delaying that thread would result in very high slowdown compared to delaying a memory-intensive thread.
To achieve both objectives, we use the “shortest job first” principle. Shortest job first scheduling has been proven to provide the optimal throughput in generalized machine scheduling theory. The controller estimates each thread’s stall-time within the batch (assuming the thread is run alone). And, it ranks a thread higher if the thread has a short stall time.

## Slide 53: Shortest Stall-Time First Ranking
Maximum number of marked requests to any bank (max-bank-load)
  Rank thread with lower max-bank-load higher (~ low stall-time)
Total number of marked requests (total-load)
  Breaks ties: rank thread with lower total-load higher
T2
T3
T1
T0
Bank 0
Bank 1
Bank 2
Bank 3
T3
T3
T1
T3
T2
T2
T1
T2
T1
T0
T2
T0
T3
T2
T3
T3
T3
T3
 | max-bank-load | total-load
T0 | 1 | 3
T1 | 2 | 4
T2 | 2 | 6
T3 | 5 | 9
Ranking:
T0 > T1 > T2 > T3
Notes:     How is this exactly done? The controller keeps track of two values for each thread. First, the maximum number of marked requests from the thread to any bank. This is called max-bank-load. A lower value of this correlates with low stall time (and less memory intensiveness). As a result the scheduler ranks a thread with lower max-bank-load higher than a thread with higher max-bank load.
    If the max-bank-load of the two threads are equal, the scheduler uses another value it keeps track of to break the ties. It keeps the total number of requests in the batch from each thread. This is called total-load. If a thread has lower total-load it is less intensive, therefore it is ranked higher.
    Let’s take a look at these concepts with an example. Assume these are the requests within the batch.
    T0 has at most 1 request to any bank, so its max-bank-load is 1. Its total-load is 3 since it has total 3 marked requests.
    T1 has at most 2 requests to any bank so its max-bank-load is 2. Its total load is 6.
    T2 similarly has a max-bank-load of 2, but its total load is higher.
    Finally, T3 has a maximum of 5 requests to Bank 3. Therefore, its max-bank load is 5.
    Because T1 has the smallest max-bank-load, it is ranked highest. The scheduler ranks T1 higher than T2 because T1 has fewer total requests. The most memory intensive thread, T2 is ranked the lowest.
    ----------------------------
    Insight: Memory-intensive threads can be delayed more within a batch since their baseline stall-time is high
    How do you break the ties? A thread with lower total-load is ranked higher
    Goal: Finish non-intensive threads first and fill in the gaps in parallelism as much as possible
    Shortest job first within a batch might seem unfair, but remember the batch boundaries. Less intensive threads will be penalized across batches because if their requests are not marked, they cannot be serviced. Shortest job first balances this delay caused to the less intensive threads
Thread 0 has at most one request to any bank
Thread 1 has at most 2: it has two requests to Bank 0.
Thread 2 has at most 2 as well.
Thread 3 has max number of requests to Bank 3 (5 reqs)

## Slide 54: Example Within-Batch Scheduling Order
7
5
3
T2
T3
T1
T0
Bank 0
Bank 1
Bank 2
Bank 3
T3
T3
T1
T3
T2
T2
T1
T2
T1
T0
T2
T0
T3
T2
T3
T3
T3
T3
Baseline Scheduling
Order (Arrival order)
PAR-BS Scheduling
Order
T2
T3
T1
T0
Bank 0
Bank 1
Bank 2
Bank 3
T3
T3
T1
T3
T2
T2
T1
T2
T1
T0
T2
T0
T3
T2
T3
T3
T3
T3
T0 | T1 | T2 | T3
4 | 4 | 5 | 7
AVG: 5 bank access latencies
AVG: 3.5 bank access latencies
Stall times
T0 | T1 | T2 | T3
1 | 2 | 4 | 7
Stall times
Time
1
2
4
6
Ranking: T0 > T1 > T2 > T3
1
2
3
4
5
6
7
Time
Notes: How does this ranking affect the scheduling order? Let’s take a look at this pictorially.
First, let’s look at the baseline scheduler. I will show the time at which the requests are serviced, where time is expressed abstractly in terms of bank access latency. In the baseline scheduler, the batched requests are serviced in their arrival order. As a result, the last request of T0 is serviced after 4 bank access latencies, the last request of T1 is also serviced after 4 bank access latencies. Consequently, the average stall time of the threads is approximately 5 bank access latencies within this batch of requests.
If we use PAR-BS to rank the threads, the scheduler will prioritize requests based on their thread-rank order, which I showed before. It prioritizes T0’s requests first (as shown in the ranking order). As a result, T0’s requests complete after 1 bank access latency. T1’s requests are serviced after 2 bank access latencies. T2’s requests are serviced after 4 bank access latencies.
Note that the bank parallelism of each thread is preserved as much as possible. Because of this, the average stall time reduces by 30%. Thus, system throughput improves.
Also note that, to keep this example simple, I assumed there are no row-buffer hits. A more complicated example with row-buffer hits is provided in the paper, and I encourage you to look at it.
--------------------------------------
Time is in bank access latencies (note that this is an approximation to demonstrate the idea… real DRAM system is much more complex than this…)
Last request from a thread is scheduled at TIME

## Slide 55: Putting It Together: PAR-BS Scheduling Policy
PAR-BS Scheduling Policy
  (1) Marked requests first
  (2) Row-hit requests first
  (3) Higher-rank thread first (shortest stall-time first)
  (4) Oldest first
Three properties:
  Exploits row-buffer locality and intra-thread bank parallelism
  Work-conserving
    Services unmarked requests to banks without marked requests
  Marking-Cap is important
    Too small cap: destroys row-buffer locality
    Too large cap: penalizes memory non-intensive threads
Many more trade-offs analyzed in the paper
Batching
Parallelism-aware
within-batch
scheduling
Notes: The resulting scheduling policy of our mechanism is based on four simple prioritization rules.
Marked requests are prioritized over others. This is the batching component.
Within a batch, row-hit requests are prioritized over others to exploit row-buffer locality (as in FR-FCFS). Then, higher-ranked threads’ requests are prioritized over lower ranked threads’ requests (to preserve each thread’s bank parallelism). Finally all else being equal, older requests are prioritized over others.
This scheduling policy has three properties.
First, it exploits both row-buffer locality and intra-thread bank parallelism. I assumed no row buffer hits in the previous example, to keep it simple, but this is taken into account in our scheduling algorithm. There is a balance between exploiting row buffer locality and bank parallelism, and our scheduling algorithm tries to achieve this balance. An example with row hits is provided in the paper.
Second, it is work conserving. It services unmarked requests in banks without marked requests.
Third, and I will not go into much detail on this, Marking-Cap is the most important parameter. Remember that the Marking-Cap determines how many requests from each thread to each bank can be admitted into a batch. If the cap is too small, too few requests from each thread are admitted into the batch. As a result, a thread’s row buffer locality cannot be exploited. If the cap is too large too many requests from intensive threads enter the batch, which slows down non-intensive threads.
Many other similar trade-offs are analyzed in the paper and I encourage you to read it.

## Slide 56: Hardware Cost
<1.5KB storage cost for
  8-core system with 128-entry memory request buffer
No complex operations (e.g., divisions)
Not on the critical path
  Scheduler makes a decision only every DRAM cycle
Notes: The implementation of PAR-BS is relatively simple. It requires three pieces of logic. Marking logic and thread ranking logic are utilized only when a new batch is formed. Extensions to request prioritization logic are needed to take into account the marked status and the thread-rank of each request.
There are no complex operations and the logic is not on the critical path of execution.
Our implementation requires less than 1.5KB storage cost within a reasonably large system with 8 cores.
More details are provided in the paper.

## Slide 57: Unfairness on 4-, 8-, 16-core Systems
Unfairness = MAX Memory Slowdown / MIN Memory Slowdown [MICRO 2007]
1.11X
1.08X
1.11X
Notes: This graph compares the five schedulers in terms of unfairness averaged over all workloads run on the 4, 8, and 16 core systems. Unfairness is computed as the max memory slowdown in the system divided by the minimum memory slowdown in the system. PAR-BS reduces unfairness significantly compared to the best previous scheduler, STFM, on all systems.
We conclude that the combination of batching and shortest stall-time first within batch scheduling provides good fairness without the need to explicitly estimate each thread’s slowdown and adjust scheduling policy based on that.

## Slide 58: System Performance (Hmean-speedup)
8.3%
6.1%
5.1%
Notes: This graph compares the system performance provided by the five schedulers. Performance is normalized to that of the baseline FR-FCFS scheduler. PAR-BS also improves system performance compared to the best previous scheduler, STFM, on all systems. In the 4-core system, PAR-BS provides an 8.3% performance improvement. The main reason is that PAR-BS improves each thread’s bank level parallelism: as a result, it reduces the average stall time per each request by 7.1% in the four core system (from 301 cycles to 281 cycles)

## Slide 59: PAR-BS Pros and Cons
Upsides:
  First scheduler to address bank parallelism destruction across multiple threads
  Simple mechanism (vs. STFM)
  Batching provides fairness
  Ranking enables parallelism awareness
Downsides:
  Does not always prioritize the latency-sensitive applications

## Slide 60: More on PAR-BS
Onur Mutlu and Thomas Moscibroda, "Parallelism-Aware Batch Scheduling: Enhancing both Performance and Fairness of Shared DRAM Systems" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 63-74, Beijing, China, June 2008. [Summary] [Slides (ppt)]

## Slide 61: ATLAS Memory Scheduler
Yoongu Kim, Dongsu Han, Onur Mutlu, and Mor Harchol-Balter, "ATLAS: A Scalable and High-Performance
Scheduling Algorithm for Multiple Memory Controllers" 16th International Symposium on High-Performance Computer Architecture (HPCA),
Bangalore, India, January 2010. Slides (pptx)
ATLAS HPCA 2010 Talk

## Slide 62: ATLAS: Summary
Goal: To maximize system performance
Main idea: Prioritize the thread that has attained the least service from the memory controllers (Adaptive per-Thread Least Attained Service Scheduling)
  Rank threads based on attained service in the past time interval(s)
  Enforce thread ranking in the memory scheduler during the current interval
Why it works: Prioritizes “light” (memory non-intensive) threads that are more likely to keep their cores busy

## Slide 63: System Throughput: 24-Core System
Chart: System throughput
| 1 | 2 | 4 | 8 | 16 | Memory controllers
FCFS | 4.4802 | 7.1516 | 9.4221 | 11.9271 | 14.3903
FR_FCFS | 4.5363 | 7.4098 | 9.452 | 11.9951 | 14.4325
STFM | 5.6079 | 7.2459 | 9.2466 | 11.8455 | 14.376
PAR-BS | 5.3181 | 7.9826 | 9.8744 | 12.148 | 14.4958
ATLAS | 6.2242 | 8.7648 | 10.6995 | 12.8597 | 15.0021
System throughput = ∑ Speedup
ATLAS consistently provides higher system throughput than all previous scheduling algorithms
17.0%
9.8%
8.4%
5.9%
3.5%
System throughput
# of memory controllers

## Slide 64: System Throughput: 4-MC System
Chart: System throughput
| 4 | 8 | 16 | 24 | 32 | Cores
PAR-BS | 3.2707 | 4.8105 | 7.5074 | 9.8744 | 11.6321
ATLAS | 3.307 | 4.9796 | 7.8079 | 10.6995 | 12.8871
# of cores increases  ATLAS performance benefit increases
1.1%
3.5%
4.0%
8.4%
10.8%
System throughput
# of cores

## Slide 65: ATLAS Pros and Cons
Upsides:
  Good at improving overall throughput (compute-intensive threads are prioritized)
  Low complexity
  Coordination among controllers happens infrequently
Downsides:
  Lowest/medium ranked threads get delayed significantly  high unfairness

## Slide 66: More on ATLAS Memory Scheduler
Yoongu Kim, Dongsu Han, Onur Mutlu, and Mor Harchol-Balter, "ATLAS: A Scalable and High-Performance Scheduling Algorithm for Multiple Memory Controllers" Proceedings of the 16th International Symposium on High-Performance Computer Architecture (HPCA), Bangalore, India, January 2010. Slides (pptx)

## Slide 67: TCM: Thread Cluster Memory Scheduling
Yoongu Kim, Michael Papamichael, Onur Mutlu, and Mor Harchol-Balter, "Thread Cluster Memory Scheduling:
Exploiting Differences in Memory Access Behavior" 43rd International Symposium on Microarchitecture (MICRO),
pages 65-76, Atlanta, GA, December 2010. Slides (pptx) (pdf)
TCM Micro 2010 Talk

## Slide 68: Previous Scheduling Algorithms are Biased
No previous memory scheduling algorithm provides both the best fairness and system throughput
Chart: Weighted Speedup
| 7.21 | 8.1660000000000004 | 8.26 | 8.527000000000001 | 8.7780000000000005
FCFS | 8.513
FRFCFS | 14.18
STFM | 9.245
PAR-BS | 7.418
ATLAS | 11.52
System throughput bias
Fairness bias
Ideal
Better system throughput
Better fairness
24 cores, 4 memory controllers, 96 workloads
Notes: The problem is that previously proposed scheduling algorithms are biased.
Shown here is a plot, where the x-axis is weighted speedup, a metric of system throughput and system throughput increases as you move towards the right on the x-axis.
The y-axis is maximum slowdown, which is the slowdown of the most unfairly treated thread within a workload. Correspondingly, fairness increases as you move downwards on the y-axis.
Ideally, a memory scheduling algorithm would be situated towards the lower right part of the graph where fairness and system throughput are both high.
However, some previous algorithms are biased towards system throughput, whereas some are biased towards fairness, while others are optimized for neither.
The takeaway is that no previous memory scheduling algorithm provides both the best fairness and system throughput.

## Slide 69: Throughput vs. Fairness
  Take turns accessing memory
Fairness biased approach
thread C
thread B
thread A
less memory intensive
higher
priority
  Prioritize less memory-intensive threads
Throughput biased approach
  Good for throughput
starvation  unfairness
thread C
thread B
thread A
  Does not starve
not prioritized 
reduced throughput
Single policy for all threads is insufficient
Notes: So why do previous algorithms fail?
On the one hand there is the throughput biased approach that prioritizes less memory-intensive threads.
Servicing memory requests from such threads allow them to make progress in the processor, increasing throughput.
However, the most memory-intensive thread, thread C, remains persistently deprioritized and and becomes prone to starvation causing large slowdowns and, ultimately, unfairness.
On the other hand there is the fairness biased approach where threads take turns accessing the memory.
In this case, the most memory-intensive thread does not starve.
However, the least memory-intensive thread, thread A, is not prioritized, leading to reduced throughput.
As you can see, a single policy applied to all threads is insufficient since different threads have different memory access needs.

## Slide 70: Achieving the Best of Both Worlds
thread
thread
higher
priority
thread
thread
thread
thread
thread
thread
  Prioritize memory-non-intensive threads
For Throughput
  Unfairness caused by memory-intensive being prioritized over each other
    Shuffle thread ranking
  Memory-intensive threads have different vulnerability to interference
    Shuffle asymmetrically
For Fairness
thread
thread
thread
thread
Notes: So how do we achieve the best of both worlds? Our algorithm is based on the following insights:
First, we would like to prioritize the memory-non-intensive threads to increase system throughput.
Doing so does not degrade unfairness, since memory-non-intensive threads are inherently “light” and rarely cause interference for the memory-intensive threads.
For fairness, we discovered that unfairness is usually caused when one memory-intensive thread is prioritized over another.
As we’ve seen, the most deprioritized thread can starve.
To address this problem, we would like to shuffle their priority so that no single thread is persistently prioritized over another thread.
However, memory-intensive threads are not created equal.
They have different vulnerability to memory interference.
To address their differences, shuffling should be performed in an asymmetric manner.

## Slide 71: Thread Cluster Memory Scheduling [Kim+ MICRO’10]
Group threads into two clusters
Prioritize non-intensive cluster
Different policies for each cluster
thread
Threads in the system
thread
thread
thread
thread
thread
thread
Non-intensive
cluster
Intensive cluster
thread
thread
thread
Memory-non-intensive
Memory-intensive
Prioritized
higher
priority
higher
priority
Throughput
Fairness
Notes: Our algorithm, Thread Cluster Memory Scheduling, first groups threads into two clusters.
Among the threads executing in the system, some are memory-non-intensive whereas some are memory-intensive.
We isolate the memory-non-intensive threads into the non-intensive cluster and the memory-intensive threads into the intensive cluster.
This is so that we can apply different policies for different threads.
Subsequently, we prioritize the non-intensive cluster over the intensive cluster since the non-intensive threads have greater potential for making progress IN THEIR CORES [ONUR].
Finally, we apply different policies within each cluster, one optimized for throughput and the other for fairness.

## Slide 72: TCM Outline
1. Clustering
Notes: First, I will talk about how threads are grouped into two clusters.

## Slide 73: Clustering Threads
Step1 Sort threads by MPKI (misses per kiloinstruction)
thread
thread
thread
thread
thread
thread
higher
MPKI
T
α < 10% ClusterThreshold
Intensive
cluster
αT
Non-intensive
cluster
T = Total memory bandwidth usage
Step2 Memory bandwidth usage αT divides clusters
Notes: To group threads into two clusters, we first sort threads according to their MPKI, which stands for last-level cache-misses per kiloinstruction and is a metric of memory intensity.
After sorting, the leftmost thread is the thread with the lowest MPKI.
We then define a quantity called T, which is the total memory bandwidth usage across all threads.
Second, we form the non-intensive cluster by including threads whose bandwidth usage sums up to a certain fraction of the memory bandwidth usage.
That fraction is defined by a parameter called the ClusterThreshold. I will show later in the presentation how adjusting this parameter we can trade off between throughput and fairness.
Lastly, the remaining threads become the intensive cluster.

## Slide 74: TCM Outline
1. Clustering
2. Between
Clusters
Notes: Now I will talk about the scheduling policy between the two clusters.

## Slide 75: Prioritization Between Clusters
  Prioritize non-intensive cluster
Increases system throughput
  Non-intensive threads have greater potential for making progress
Does not degrade fairness
  Non-intensive threads are “light”
  Rarely interfere with intensive threads
>
priority
Notes: Between the two clusters, we statically prioritize the non-intensive cluster [ONUR: fixed plural  singular] so that non-intensive threads’ [ONUR: fixed wording] memory requests are serviced first.
This increases system throughput because non-intensive threads have greater potential for making progress BY QUICKLY RETURNING TO COMPUTE PERIODS IN THEIR CORES [ONUR].
Doing so does not degrade fairness, since non-intensive threads are “light” and consequently rarely interfere with intensive threads. [ONUR: removed “by design”… can be confusing if the listener is not in the right mindset]

## Slide 76: TCM Outline
1. Clustering
2. Between
Clusters
3. Non-Intensive
Cluster
Throughput
Notes: Now I’ll discuss the scheduling policies applied within each cluster, starting first with the non-intensive cluster.

## Slide 77: Non-Intensive Cluster
Prioritize threads according to MPKI
Increases system throughput
  Least intensive thread has the greatest potential for making progress in the processor
thread
thread
thread
thread
higher
priority
lowest MPKI
highest MPKI
Notes: Within the memory non-intensive cluster, threads are prioritized according to their memory intensity where the least intensive thread receives the highest priority. [ONUR: replaced latency-sensitive]
This is, again, to increase system throughput. The least intensive thread has the greatest potential for making progress.

## Slide 78: TCM Outline
1. Clustering
2. Between
Clusters
3. Non-Intensive
Cluster
4. Intensive
Cluster
Throughput
Fairness
Notes: Now I’ll talk about the scheduling policy applied within the intensive cluster.

## Slide 79: Intensive Cluster
Periodically shuffle the priority of threads
Is treating all threads equally good enough?
BUT: Equal turns ≠ Same slowdown
thread
thread
thread
  Increases fairness
  Most prioritized
higher
priority
thread
thread
thread
Notes: Within the intensive cluster, we periodically shuffle the priority of threads.
By shuffling, we can increase fairness, since every thread is given a fair chance of being the most prioritized.
Treating all threads in an such an equal manner may be good enough in some cases.
But we noticed that in other cases, giving each thread equal turns does not necessarily lead to equal slowdowns.
Specifically, threads are not created equal and some threads are more easily slowed down than others.

## Slide 80: Case Study: A Tale of Two Threads
Chart: Slowdown
| random-access | streaming
Series 1 | 11 | 1
Case Study: Two intensive threads contending
  random-access
  streaming
Prioritize random-access
Prioritize streaming
random-access thread is more easily slowed down
Chart: Slowdown
| random-access | streaming
Series 1 | 1 | 7
7x
prioritized
1x
11x
prioritized
1x
Which is slowed down more easily?
Notes: We illustrate how some threads are more easily slowed down than others using a case study, where two memory-intensive threads are contending for memory: a random-access thread and a streaming thread.
Which of these two threads is slowed down more easily?
In the first case, we prioritize the random-access thread and see that the streaming thread is slowed down by a factor of 7.
In the second case, we prioritize the streaming thread and see that the random-access thread is slowed down by a factor of 11.
Clearly, comparing the two cases, we see that the random-access threads is more easily slowed down.

## Slide 81: Why are Threads Different?
random-access
streaming
req
req
req
req
Bank 1
Bank 2
Bank 3
Bank 4
Memory
rows
All requests parallel
High bank-level parallelism
All requests  Same row
High row-buffer locality
req
req
req
req
activated row
req
req
req
req
req
req
req
req
stuck
Vulnerable to interference
Notes: ONUR: Again, if you prefer, you can use “vulnerable” instead of “susceptible.”
So why are these two threads different?
To explain their difference, we must examine their memory access behavior.
First, the memory comprises multiple memory banks which can be accessed in parallel. [ONUR: removed structurally]
Additionally, each bank is basically a two-dimensional bit-array and comprises multiple rows.
The random access thread distributes its memory requests, to different banks.
Across the banks, the requests are serviced concurrently and their individual latencies are overlapped.
Therefore, the random-access thread has high bank-level parallelism.
On the other hand, the streaming thread sends its memory requests to the same bank.
There it is serviced at the same row over and over again.
When consecutive requests are serviced at the same row, it is called a row-buffer hit and has a lower latency.
Therefore, the streaming thread has higher row-buffer locality.
What would happen if we put those threads together?
For the purpose of illustration, we will assume that the streaming thread is prioritized.
You can see that the random-access thread’s request becomes stuck behind those of the streaming thread at Bank 3.
This breaks the bank-level parallelism of the random-access thread and serializes its latency, leading to reduced performance.
This is why, the random-access thread is more susceptible to interference.
If the two threads were prioritized the other way around, the streaming thread would not be interfered with as much, since the random-access thread has only a single request to Bank 3.

## Slide 82: TCM Outline
1. Clustering
2. Between
Clusters
3. Non-Intensive
Cluster
4. Intensive
Cluster
Fairness
Throughput

## Slide 83: Niceness
How to quantify difference between threads?
  Vulnerability to interference
Bank-level parallelism
  Causes interference
Row-buffer locality
+
Niceness
-
Niceness
High
Low

## Slide 84: TCM: Quantum-Based Operation
Time
Previous quantum (~1M cycles)
During quantum:
Monitor thread behavior
Memory intensity
Bank-level parallelism
Row-buffer locality
Beginning of quantum:
Perform clustering
Compute niceness of intensive threads
Current quantum
(~1M cycles)
Shuffle interval
(~1K cycles)
Notes: Clustering is performed at regular time intervals called quanta.
THIS IS DONE [ONUR] to account for phase changes in threads’ memory access behavior.
During A [ONUR] quantum, TCM monitors each thread’s memory access behavior:
memory intensity, bank-level parallelism, and row-buffer locality.
At the beginning of the next quantum, TCM is invoked to perform clustering and calculate niceness for the intensive threads.
Throughout the quantum, shuffling of the intensive threads is performed periodically.

## Slide 85: TCM: Scheduling Algorithm
Highest-rank: Requests from higher ranked threads prioritized
    Non-Intensive cluster > Intensive cluster
    Non-Intensive cluster: lower intensity  higher rank
    Intensive cluster: rank shuffling
Row-hit: Row-buffer hit requests are prioritized
Oldest: Older requests are prioritized
Notes: To bring it all together, TCM comprises three simple request prioritization rules.
The first is the highest-rank rule, where requests from higher ranked threads are prioritized.
The intensive cluster is prioritized over the non-intensive cluster TO IMPROVE SYSTEM [ONUR] throughput.
Within the intensive cluster, threads are assigned higher rank in the order of decreasing intensity. This, again, is to increase SYSTEM [ONUR] throughput.
Within the non-intensive cluster, the rank of threads are periodically shuffled and does not stay constant, TO ACHIEVE FAIRNESS [ONUR].
As a tie-breaker, the second rule is row-hit where row-buffer hitting requests are prioritized.
Lastly, all else being the same, we prioritize the oldest request.

## Slide 86: TCM: Implementation Cost
Required storage at memory controller (24 cores)
No computation is on the critical path
Thread memory behavior | Storage
MPKI | ~0.2kb
Bank-level parallelism | ~0.6kb
Row-buffer locality | ~2.9kb
Total | < 4kbits
Notes: ONUR: Have a separate bullet saying “No computation is on the processor critical path; Can be approximated.”
Basically, DRAM latency is very long so we can afford to do this computation especially since we are doing it over intervals.
You can have 4 cores in the first bullet and remove the subbullet.

## Slide 87: Previous Work
FRFCFS [Rixner et al., ISCA00]: Prioritizes row-buffer hits
  Thread-oblivious  Low throughput & Low fairness
STFM [Mutlu et al., MICRO07]: Equalizes thread slowdowns
  Non-intensive threads not prioritized  Low throughput
PAR-BS [Mutlu et al., ISCA08]: Prioritizes oldest batch of requests while preserving bank-level parallelism
  Non-intensive threads not always prioritized  Low throughput
ATLAS [Kim et al., HPCA10]: Prioritizes threads with less memory service
  Most intensive thread starves  Low fairness

## Slide 88: TCM: Throughput and Fairness
Chart: Weighted Speedup
| 8.1660000000000004 | 8.26 | 8.527000000000001 | 8.7780000000000005 | 9.1790000000000003
FRFCFS | 14.18
STFM | 9.245
PAR-BS | 7.418
ATLAS | 11.52
TCM | 7.074
Better system throughput
Better fairness
24 cores, 4 memory controllers, 96 workloads
TCM, a heterogeneous scheduling policy,
provides best fairness and system throughput
Notes: This figure shows the performance of the four previous scheduling algorithms in addition to TCM, averaged over 96 workloads.
FRFCFS has low system throughput and fairness.
STFM and PAR-BS is biased towards fairness, while ATLAS is biased towards system throughput.
TCM lies towards the lower right part of the figure and provides the best fairness and system throughput.
Compared to ATLAS, TCM provides approx 5% better throughput and 39% better fairness.
Compared to PAR-BS, TCM provides approx 5% better fairness and 8% better throughput.

## Slide 89: TCM: Fairness-Throughput Tradeoff
Chart: Weighted Speedup
| 12.73 | 13 | 13.03 | 13.04 | 12.97 | 12.81 | 12.66 | 12.48 | 13.11 | 13.21 | 13.21 | 13.19 | 13.16 | 13.06 | 13.6 | 13.76 | 13.61 | 13.68 | 13.65 | 13.62 | 14.49 | 14.58 | 14.8 | 14.84 | 14.83 | 14.43 | 14.04 | 14.4 | 14.63 | 14.79 | 14.92
FRFCFS | 9.825 | 6.73 | 5.84 | 5.38 | 5 | 5.07 | 5.5 | 5.73
STFM | 5.949 | 6.215 | 6.423 | 6.923 | 6.953 | 7.263
PAR-BS | 5.999 | 5.449 | 5.423 | 5.075 | 4.905 | 4.82
ATLAS | 7.018 | 7.139 | 7.422 | 7.501 | 7.552 | 7.458
TCM | 4.843 | 4.952 | 5.258 | 5.503 | 5.727
When configuration parameter is varied…
Adjusting ClusterThreshold
TCM allows robust fairness-throughput tradeoff
STFM
PAR-BS
ATLAS
TCM
Better system throughput
Better fairness
FRFCFS

## Slide 90: Operating System Support
ClusterThreshold is a tunable knob
  OS can trade off between fairness and throughput
Enforcing thread weights
  OS assigns weights to threads
  TCM enforces thread weights within each cluster

## Slide 91: Conclusion
No previous memory scheduling algorithm provides both high system throughput and fairness
  Problem: They use a single policy for all threads
TCM groups threads into two clusters
  Prioritize non-intensive cluster  throughput
  Shuffle priorities in intensive cluster  fairness
  Shuffling should favor nice threads  fairness
TCM provides the best system throughput and fairness

## Slide 92: TCM Pros and Cons
Upsides:
  Provides both high fairness and high performance
  Caters to the needs for different types of threads (latency vs. bandwidth sensitive)
  (Relatively) simple
Downsides:
  Scalability to large buffer sizes?
  Robustness of clustering and shuffling algorithms?
  Ranking is still too complex?

## Slide 93: More on TCM
Yoongu Kim, Michael Papamichael, Onur Mutlu, and Mor Harchol-Balter, "Thread Cluster Memory Scheduling: Exploiting Differences in Memory Access Behavior" Proceedings of the 43rd International Symposium on Microarchitecture (MICRO), pages 65-76, Atlanta, GA, December 2010. Slides (pptx) (pdf)

## Slide 94: The Blacklisting Memory Scheduler
Lavanya Subramanian, Donghyuk Lee, Vivek Seshadri, Harsha Rastogi, and Onur Mutlu, "The Blacklisting Memory Scheduler: Achieving High Performance and Fairness at Low Cost" Proceedings of the 32nd IEEE International Conference on Computer Design (ICCD),
Seoul, South Korea, October 2014. [Slides (pptx) (pdf)]

## Slide 95: Tackling Inter-Application Interference: Application-aware Memory Scheduling
Monitor
Rank
Highest Ranked AID
Enforce
Ranks
Full ranking increases
critical path latency and area significantly to improve
performance and fairness
4
3
2
1
2
4
3
1
Req 1
1
Req 2
4
Req 3
1
Req 4
1
Req 5
3
Req 7
1
Req 8
3
Request Buffer
Req 5
2
Request
App. ID (AID)
=
=
=
=
=
=
=
=
Notes: The key principles behind application-aware memory request scheduling are to first monitor applications’ memory access characteristics, rank applications based on these access characteristics. A memory access characteristic that several application aware schedulers use is memory intensity (the rate at which the application generates accesses to memory). Low memory intensity applications are ranked higher.
Once a ranking is computed, requests are prioritized at the memory controller to obey this ranking. For instance, in this example, the blue application here is the highest ranked. So, its requests are given highest priority.
In this work, we observe that this kind of a ranking based scheduler increases critical path latency and area significantly in order to improve performance and fairness among applications.

## Slide 96: Performance vs. Fairness vs. Simplicity
Performance
Fairness
Simplicity
FRFCFS
PARBS
ATLAS
TCM
Blacklisting
Ideal
App-unaware
App-aware (Ranking)
Our Solution
(No Ranking)
Is it essential to give up simplicity to optimize for performance and/or fairness?
Our solution achieves all three goals
Very Simple
Low performance and fairness
Complex
Our Solution
Notes: This chart shows performance, fairness and simplicity on three axes. The ideal scheduler should maximize all three of these quantities. Now, let’s look at where different schedulers lie in this space.
First, let’s look at a state-of-the-art application-unaware scheduler. It is simple, but has low performance and fairness. Next, let’s look at some application-aware schedulers. This scheduler optimizes for fairness and performance, but gives up simplicity. This one optimizes for performance, but gives up simplicity and fairness. Finally, this one optimizes for both performance and fairness, but gives up simplicity. One common attribute of these application-aware schedulers is that they trade-off simplicity to achieve performance and/or fairness, since they all use a ranking-based scheme like the one I described in the previous slide.
In this work, we ask the key question, is it essential to give up simplicity in order to optimize for performance and fairness? We propose a new memory scheduling algorithm that is simple, high performance and fair, by eliminating the idea of employing a full ordered ranking among all applications.

## Slide 97: Key Observation 1: Group Rather Than Rank
Observation 1: Sufficient to separate applications into two groups, rather than do full ranking
Benefit 1: Low complexity compared to ranking
Group
Vulnerable
Interference
Causing
>
Monitor
Rank
4
3
2
1
2
4
3
1
4
2
3
1
Benefit 2: Lower slowdowns than ranking
Notes: We first observe that it is sufficient to separate applications into two groups, rather than perform a full ordered ranking across all applications.
Like I described earlier, application-aware memory schedulers typically monitor applications’ memory access characteristics and perform a full ordered ranking across all applications based on their memory access characteristics. We observe that such a full ordered ranking is not necessary. Instead, applications can be classified into only two groups, one containing vulnerable applications and the other containing interference-causing applications. Requests from the vulnerable application group are prioritized over requests from the interference-causing application group. Apart from this single level of prioritization, there is no ranking between applications’ requests within a group.
One clear benefit of such a grouping-based scheduler is reduced complexity. There is no need to rank or sort all applications. Furthermore, the enforcement of a single level of priority incurs much lower complexity than the enforcement of a full ordered ranking.

## Slide 98: Key Observation 1: Group Rather Than Rank
Observation 1: Sufficient to separate applications into two groups, rather than do full ranking
Group
Vulnerable
Interference
Causing
>
Monitor
Rank
4
3
2
1
2
4
3
1
4
2
3
1
How to classify applications into groups?
Notes: We first observe that it is sufficient to separate applications into two groups, rather than perform a full ordered ranking across all applications.
Like I described earlier, application-aware memory schedulers typically monitor applications’ memory access characteristics and perform a full ordered ranking across all applications based on their memory access characteristics. We observe that such a full ordered ranking is not necessary. Instead, applications can be classified into only two groups, one containing vulnerable applications and the other containing interference-causing applications. Requests from the vulnerable application group are prioritized over requests from the interference-causing application group. Apart from this single level of prioritization, there is no ranking between applications’ requests within a group.
One clear benefit of such a grouping-based scheduler is reduced complexity. There is no need to rank or sort all applications. Furthermore, the enforcement of a single level of priority incurs much lower complexity than the enforcement of a full ordered ranking.

## Slide 99: Key Observation 2
Observation 2: Serving a large number of consecutive requests from an application causes interference
Basic Idea:
Group applications with a large number of consecutive requests as interference-causing  Blacklisting
Deprioritize blacklisted applications
Clear blacklist periodically (1000s of cycles)
Benefits:
Lower complexity
Finer grained grouping decisions  Lower unfairness
Notes: We observe that when a large number of consecutive requests are served from an application, it interferes with other applications since their requests are delayed.
Based on this observation, we propose to group applications by monitoring the number of consecutive requests served from an application. Applications with a number of consecutive requests served are classified as interference-causing. Essentially, these applications are blacklisted. Requests from these blacklisted applications are deprioritized. This blacklist status is cleared periodically (at fine time granularities) in order to ensure that no applications are deprioritized for too long.
This kind of a grouping scheme has two main benefits. First, lower complexity compared to a scheme that monitors metrics like memory intensity on an interval basis. With this kind of a grouping scheme, only a single bit needs to be maintained for each application in order to denote its blacklist status, rather than having to count and maintain memory intensity for every application. Second, this scheme enables fine grained grouping decisions. Applications are classified into groups based on monitoring a few consecutive requests. Furthermore, this grouping is also cleared at fine time granularities. This prevents any application from being deprioritized for too long, unlike an interval based scheme that monitors memory access characteristics over a long time and then classifies applications.

## Slide 100: Performance vs. Fairness vs. Simplicity
Performance
Fairness
Simplicity
FRFCFS
FRFCFS
-
Cap
PARBS
ATLAS
TCM
Blacklisting
Ideal
Highest performance
Close to simplest
Close to fairest
Blacklisting is the closest scheduler to ideal

## Slide 101: Performance and Fairness
Chart: Performance
| 7.7947186307350647
FRFCFS | 8.2987
FRFCFS-Cap | 6.143
PARBS | 5.6852
ATLAS | 13.9188
TCM | 8.3287
Blacklisting | 6.5405
Ideal
5%
21%
(Higher is better)
(Lower is better)
1. Blacklisting achieves the highest performance
2. Blacklisting balances performance and fairness
Notes: First, let me present performance and fairness results.
Here is a pareto plot showing performance on the x-axis and unfairness on the y-axis. The ideal memory scheduler would maximize performance while minimizing unfairness. Let’s look at where different schedulers lie in this space.
The FRFCFS scheduler optimizes for neither performance nor fairness. FRFCFS-Cap and PARBS reduce unfairness significantly while improving performance. Schedulers like ATLAS and TCM optimize for performance further, but at the cost of increasing unfairness. The blacklisting scheduler moves much closer to the ideal achieving both high performance and fairness. We draw two major conclusions.
First, the blacklisting memory scheduler achieves the highest performance among all previous schedulers we compare to.
Second, the blacklisting memory scheduler achieves a good balance between performance and fairness, improving performance over the best performing previous schedulers, while approaching the fairness of the fairest previous schedulers.

## Slide 102: Complexity
Chart: Critical Path Latency (ns)
| 1
FRFCFS | 41000
FRFCFS-Cap | 41003
PARBS | 98464
ATLAS | 68406
TCM | 73797
Blacklisting | 42331
43%
70%
Blacklisting reduces complexity significantly
Ideal
Notes: Next, I will present our complexity results. This plot shows critical path latency on the x-axis and scheduler area on the y-axis. The ideal scheduler would minimize both critical path latency and area.
Let’s look at where different schedulers lie in this space. The application-unaware FRFCFS scheduler has both low critical path latency and area, as we would expect. The FRFCFS-Cap scheduler which is very similar to the FRFCFS scheduler in terms of implementation, has similar area and critical path latency.
The application-aware schedulers, PARBS, ATLAS and TCM increase both critical path latency and area significantly over the application-unaware schedulers.
Our solution, the blacklisting scheduler has significantly critical path latency and area than the application-aware schedulers and is much closer in complexity to the application-unaware schedulers.
In fact, the blacklisting scheduler has 43% lower area and 70% lower critical path latency than previous application-aware schedulers.

## Slide 103: More on BLISS (I)
Lavanya Subramanian, Donghyuk Lee, Vivek Seshadri, Harsha Rastogi, and Onur Mutlu, "The Blacklisting Memory Scheduler: Achieving High Performance and Fairness at Low Cost" Proceedings of the 32nd IEEE International Conference on Computer Design (ICCD), Seoul, South Korea, October 2014. [Slides (pptx) (pdf)]

## Slide 104: More on BLISS: Longer Version
Lavanya Subramanian, Donghyuk Lee, Vivek Seshadri, Harsha Rastogi, and Onur Mutlu, "BLISS: Balancing Performance, Fairness and Complexity in Memory Access Scheduling" IEEE Transactions on Parallel and Distributed Systems (TPDS), to appear in 2016. arXiv.org version, April 2015. An earlier version as SAFARI Technical Report, TR-SAFARI-2015-004, Carnegie Mellon University, March 2015. [Source Code]

## Slide 105: Staged Memory Scheduling
Rachata Ausavarungnirun, Kevin Chang, Lavanya Subramanian, Gabriel Loh, and Onur Mutlu, "Staged Memory Scheduling: Achieving High Performance
and Scalability in Heterogeneous Systems” 39th International Symposium on Computer Architecture (ISCA),
Portland, OR, June 2012.
SMS ISCA 2012 Talk

## Slide 106: SMS: Executive Summary
Observation: Heterogeneous CPU-GPU systems require memory schedulers with large request buffers
Problem: Existing monolithic application-aware memory scheduler designs are hard to scale to large request buffer sizes
Solution: Staged Memory Scheduling (SMS)
  decomposes the memory controller into three simple stages:
  1) Batch formation: maintains row buffer locality
  2) Batch scheduler: reduces interference between applications
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness
Notes: We observe that Heterogeneous CPU-GPU systems require memory schedulers with large request buffers and this becomes a problem for existing monolithic application-aware memory scheduler designs because they are hard to scale to large request buffer size
Our Solution, staged memory scheduling, decomposes MC into three simpler stages:
  1) Batch formation: maintains row buffer locality by forming batches of row-hitting requests.
  2) Batch scheduler: reduces interference between applications by picking the next batch to prioritize.
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness, especially in heterogeneous CPU-GPU systems.

## Slide 107: SMS: Staged Memory Scheduling
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Batch Scheduler
Stage 1
Stage 2
Stage 3
Req
Monolithic Scheduler
Batch Formation
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: With these key observations, we will show how we can decouple a monolithic schedulers into a simpler design through <click> stage 1, the batch formation, <click> stage 2, the batch scheduler, <click> stage 3, the DRAM command scheduler

## Slide 108: SMS: Staged Memory Scheduling
Stage 1
Stage 2
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Batch Scheduler
Batch Formation
Stage 3
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: Now, let me explain how the batch formation works …

## Slide 109: Putting Everything Together
Current Batch Scheduling Policy
SJF
Current Batch Scheduling Policy
RR
Batch Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Core 1
Core 2
Core 3
Core 4
Stage 1:
Batch
Formation
Stage 3: DRAM Command Scheduler
GPU
Stage 2:
Notes: In this example, the system consist of 4 CPU cores and a GPU, and the color represent a row the request wants to access. Similar color means these requests want to access the same row.
In the batch formation stage, memory requests that access the same row will be batched.
<click>
One criteria that a batch becomes ready to be scheduled is when the next request is going to a different row, as illustrated in this example at core 2 and core 3. <click click>
Another criteria is when the timeout for the batch formation expires.
This batching process will happen across all cores including the GPU
<click>
<click> and how the batch scheduler will select one of these front batch to send to <click> the DRAM command scheduler.
The scheduler can either use a shortest job poilcy
<click> which will pick this purple request because it is from an application with the fewest number of requests.
Or a round-robin policy
<click>
Whenever the bank is ready to schedule a next request. DRAM command scheduler will schedule the requests in an in-order manner.
<click>
Now that I told you about how SMS works, let me tell you about the complexity of SMS
<click … transition>

## Slide 110: Complexity
Compared to a row hit first scheduler, SMS consumes*
  66% less area
  46% less static power
Reduction comes from:
  Monolithic scheduler  stages of simpler schedulers
  Each stage has a simpler scheduler (considers fewer properties at a time to make the scheduling decision)
  Each stage has simpler buffers (FIFO instead of out-of-order)
  Each stage has a portion of the total buffer size (buffering is distributed across stages)
* Based on a Verilog model using 180nm library
Notes: <transition from the previous slide>
Now that I told you about how SMS works, let me tell you about the complexity of SMS.
Compared to a row hit first scheduler, which is the one of the simplest memory scheduling algorithm that has been proposed, SMS consumes 66% less area and 46% less static power
The reduction in area and static power comes from:
  Decoupling the monolithic scheduler into stages of simpler schedulers
  Each stage has simpler scheduler, which considers fewer properties at a time to make the scheduling decision
  Each stage has simpler buffers, which is a FIFO instead of out-of-order buffers
  Each stage has a portion of the total buffer size and buffering is distributed across stages

## Slide 111: Performance at Different GPU Weights
Chart: GPUweight
Best Previous
Scheduler
ATLAS
TCM
FR-FCFS
Notes: In this plot, we show the performance of SMS, compared to the best performing scheduler. Note that the best previous algorithm is different for different weights. We vary the GPU weight of 0.001 to 1000. The Y-Axis shows the system performance measured by dividing the CPU-GPU weighted speedup by the total weight to make sure it is bound between 0 and 1.

## Slide 112: Performance at Different GPU Weights
At every GPU weight, SMS outperforms the best previous scheduling algorithm for that weight
Chart: GPUweight
SMS
Best Previous
Scheduler
Notes: We found that at every GPU weight, we can configure the probablity of using shortest job first batch scheduling policy such that SMS outperforms the best previous mechanism for that weight

## Slide 113: More on SMS
Rachata Ausavarungnirun, Kevin Chang, Lavanya Subramanian, Gabriel Loh, and Onur Mutlu, "Staged Memory Scheduling: Achieving High Performance and Scalability in Heterogeneous Systems" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pptx)

## Slide 114: DASH Memory Scheduler [TACO 2016]

## Slide 115: Current SoC Architectures
Heterogeneous agents: CPUs and HWAs
  HWA : Hardware Accelerator
Main memory is shared by CPUs and HWAs  Interference
CPU
CPU
CPU
CPU
Shared Cache
HWA
HWA
HWA
DRAM Controller
DRAM
How to schedule memory requests from CPUs and HWAs
to mitigate interference?
Notes: Today’s SoCs are usually heterogeneous architecture, which integrates heterogeneous agents, like CPUs and HWAs. CPUs and HWAs share main memory, causing interference among memory requests from Cpus and HWAs. The problem for the heterogeneous systems is how to schedule memory requests from CPUs and HWAs to mitigate interference on the memory controller. We solve this problem in this work.

## Slide 116: DASH Scheduler: Executive Summary
Problem: Hardware accelerators (HWAs) and CPUs share the same memory subsystem and interfere with each other in main memory
Goal: Design a memory scheduler that improves CPU performance while meeting HWAs’ deadlines
Challenge: Different HWAs have different memory access characteristics and different deadlines, which current schedulers do not smoothly handle
  Memory-intensive and long-deadline HWAs significantly degrade CPU performance when they become high priority (due to slow progress)
  Short-deadline HWAs sometimes miss their deadlines despite high priority
Solution: DASH Memory Scheduler
  Prioritize HWAs over CPU anytime when the HWA is not making good progress
  Application-aware scheduling for CPUs and HWAs
Key Results:
  1) Improves CPU performance for a wide variety of workloads by 9.5%
  2) Meets 100% deadline met ratio for HWAs
DASH source code freely available on our GitHub
Notes: Here’s an executive summary. The problem is hardware accelerators and CPUs share the same memory subsystem and interfere with each other.
So, the goal of this work is to design a memory scheduler that improves CPU performance while meeting HWAs’ deadlines.
The challenge to achieve the goal is different HWAs have different memory access characteristics and different deadlines. For example, memory-intensive and long-deadline HWAs significantly degrade CPU performance when they become high priority due to their slow progress. On the other hand, short-deadline HWAs sometimes miss their deadlines despite high priority. Current schedulers do not smoothly handle this difference.
For solution of this challenge, DASH memory scheduler uses 3 key ideas.
First, to meet HWAs’ deadlines, DASH prioritizes HWAs over CPU anytime when the HWA is not making good progress.
Second, however, DASH tries to prevents a HWA from becoming high priority. It is OK to prioritize the HWA over a memory-intensive CPU even when the HWA is making good progress.
Third, DASH prioritizes short-deadline-HWAs over long-deadlin-HWAs and CPUs based on worst-case memory access time estimation.
As the key results, DASH improves CPU performance for a wide variety of different CPU workloads by 9.5% and it achieves 10% deadline met ratio of HWAs.

## Slide 117: Goal of Our Scheduler (DASH)
Goal: Design a memory scheduler that
  Meets GPU/accelerators’ frame rates/deadlines and
  Achieves high CPU performance
Basic Idea:
  Different CPU applications and hardware accelerators have different memory requirements
  Track progress of different agents and prioritize accordingly

## Slide 118: Key Observation: Distribute Priority for Accelerators
GPU/accelerators need priority to meet deadlines
Worst case prioritization not always the best
Prioritize when they are not on track to meet a deadline
Distributing priority over time mitigates impact of accelerators on CPU cores’ requests

## Slide 119: Key Observation: Not All Accelerators are Equal
Long-deadline accelerators are more likely to meet their deadlines
Short-deadline accelerators are more likely to miss their deadlines
Schedule short-deadline accelerators based on worst-case memory access time

## Slide 120: Key Observation: Not All CPU cores are Equal
Memory-intensive cores are much less vulnerable to interference
Memory non-intensive cores are much more vulnerable to interference
Prioritize accelerators over memory-intensive cores to ensure accelerators do not become urgent

## Slide 121: DASH Summary: Key Ideas and Results
Distribute priority for HWAs
Prioritize HWAs over memory-intensive CPU cores even when not urgent
Prioritize short-deadline-period HWAs based on worst case estimates
Improves CPU performance by 7-21%
Meets (almost) 100% of deadlines for HWAs

## Slide 122: DASH: Scheduling Policy
DASH scheduling policy
  1. Short-deadline-period HWAs with high priority
  2. Long-deadline-period HWAs with high priority
  3. Memory non-intensive CPU applications
  4. Long-deadline-period HWAs with low priority
  5. Memory-intensive CPU applications
  6. Short-deadline-period HWAs with low priority
Switch
probabilistically
Notes: We made an optimization for the scheduling policy. We switch the priorities of rank4 and 5 probabilistically and we adjust the probability for switching dynamically based on its progress. Please see the paper for the detail of this probabilistic switching of priorities.

## Slide 123: More on DASH
Hiroyuki Usui, Lavanya Subramanian, Kevin Kai-Wei Chang, and Onur Mutlu, "DASH: Deadline-Aware High-Performance Memory Scheduler for Heterogeneous Systems with Hardware Accelerators" ACM Transactions on Architecture and Code Optimization (TACO), Vol. 12, January 2016. Presented at the 11th HiPEAC Conference, Prague, Czech Republic, January 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 124: Predictable Performance: Strong Memory Service Guarantees

## Slide 125: Goal: Predictable Performance in Complex Systems
Heterogeneous agents: CPUs, GPUs, and HWAs
Main memory interference between CPUs, GPUs, HWAs
CPU
CPU
CPU
CPU
Shared Cache
GPU
HWA
HWA
DRAM and Hybrid Memory Controllers
DRAM and Hybrid Memories
How to allocate resources to heterogeneous agents
to mitigate interference and provide predictable performance?

## Slide 126: Strong Memory Service Guarantees
Goal: Satisfy performance/SLA requirements in the presence of shared main memory, heterogeneous agents, and hybrid memory/storage
Approach:
  Develop techniques/models to accurately estimate the performance loss of an application/agent in the presence of resource sharing
  Develop mechanisms (hardware and software) to enable the resource partitioning/prioritization needed to achieve the required performance levels for all applications
  All the while providing high system performance
Subramanian et al., “MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems,” HPCA 2013.
Subramanian et al., “The Application Slowdown Model,” MICRO 2015.

## Slide 127: Predictable Performance Readings (I)
Eiman Ebrahimi, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Fairness via Source Throttling: A Configurable and High-Performance Fairness Substrate for Multi-Core Memory Systems" Proceedings of the 15th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), pages 335-346, Pittsburgh, PA, March 2010. Slides (pdf)

## Slide 128: Predictable Performance Readings (II)
Lavanya Subramanian, Vivek Seshadri, Yoongu Kim, Ben Jaiyen, and Onur Mutlu, "MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA), Shenzhen, China, February 2013. Slides (pptx)

## Slide 129: Predictable Performance Readings (III)
Lavanya Subramanian, Vivek Seshadri, Arnab Ghosh, Samira Khan, and Onur Mutlu, "The Application Slowdown Model: Quantifying and Controlling the Impact of Inter-Application Interference at Shared Caches and Main Memory" Proceedings of the 48th International Symposium on Microarchitecture (MICRO), Waikiki, Hawaii, USA, December 2015. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Source Code]

## Slide 130: MISE: Providing Performance Predictability in Shared Main Memory Systems
Lavanya Subramanian, Vivek Seshadri,
Yoongu Kim, Ben Jaiyen, Onur Mutlu
Notes: Hello everyone. My name is Lavanya Subramanian.
Today, I will present “MISE: Providing perfomance …”.
This is work done in collaboration with my co-authors Vivek ….

## Slide 131: Unpredictable Application Slowdowns
Chart: Slowdown
| leslie3d (core 0) | gcc (core 1)
Slowdown | 1.9 | 1.1
Chart: Slowdown
| leslie3d (core 0) | mcf (core 1)
Slowdown | 5.4 | 2.1
An application’s performance depends on
which application it is running with
Notes: This graph shows two applications from the SPEC CPU 2006 suite, leslie3d and gcc. These applications are run on either core of a two core system and share main memory. The y-axis shows each application’s slowdown as compared to when the application is run standalone on the same system.
Now, let’s look at leslie3d. It slows down by 2x when run with gcc.
Let’s look at another case when leslie3d is run with another application, mcf. Leslie now slows down by 5.5x, while it slowed down by 2x when run with gcc. Leslie experiences different slowdowns when run with different applications.
More generally, an application’s performance depends on which applications it is running with. Such performance unpredictability is undesirable….

## Slide 132: Need for Predictable Performance
There is a need for predictable performance
  When multiple applications share resources
  Especially if some applications require performance guarantees
Example 1: In mobile systems
  Interactive applications run with non-interactive applications
  Need to guarantee performance for interactive applications
Example 2: In server systems
  Different users’ jobs consolidated onto the same server
  Need to provide bounded slowdowns to critical jobs
Our Goal: Predictable performance
in the presence of memory interference
Notes: …because there is a need for predictable performance
When multiple applications share resources and
Especially when some applications require guarantees on performance.
For example, in mobile systems, interactive applications are run with non-interactive ones.
And there is a need to provide guarantees on performance to the interactive applications.
In server systems, different users’ jobs are heavily consolidated onto the same server.
In such a scenario, there is a need to achieve bounded slowdowns for critical jobs of users.
These are a couple of examples of systems that need predictable performance.
There are many other systems (such as …) in which performance predictability is necessary.
Therefore, our goal in this work is to provide predictable performance in the presence of memory interference.

## Slide 133: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
Notes: Towards this goal, we propose to first estimate application slowdowns due to main memory interference.
And once we have accurate slowdown estimates, we propose to leverage them to control application slowdowns.

## Slide 134: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: First, let me describe the key observations that enable us to estimate application slowdowns.

## Slide 135: Slowdown: Definition
Notes: Slowdown of an application is its performance when it is run stand alone on a system to its performance when it is sharing the system with other applications.
An application’s performance when it is sharing the system with other applications can be measured in a straightforward manner. However, measuring an application’s alone performance, without actually running it alone is harder.
This is where are first observation comes in.

## Slide 136: Key Observation 1
For a memory bound application,
Performance  Memory request service rate
Chart: Normalized Request Service Rate
| 0.35860785899999997 | 0.40850773899999998 | 0.53253157500000003 | 0.58099312199999598 | 0.632877307000005 | 0.69087995400000701 | 0.72694550100000499 | 0.79635468200000004 | 0.83755898299999998 | 0.938360254 | 0.94830560700000499 | 1
omnetpp | 0.34972 | 0.39891 | 0.5217 | 0.56944 | 0.61954 | 0.67835 | 0.71425 | 0.78346 | 0.8265 | 0.928 | 0.94883 | 1
mcf | 0.34876 | 0.39942 | 0.4869 | 0.53653 | 0.54337 | 0.55102 | 0.58278 | 0.61457 | 0.65149 | 0.74316 | 0.84741 | 0.93386 | 0.9689 | 1
astar | 0.41586 | 0.48052 | 0.66786 | 0.72536 | 0.77686 | 0.79876 | 0.84877 | 0.88035 | 0.92559 | 0.95012 | 0.98596 | 1
Easy
Harder
Intel Core i7, 4 cores
Mem. Bandwidth: 8.5 GB/s
Notes: We observe that for a memory bound application, its performance is roughly proportional to the rate at which its memory requests are serviced.
This plot shows the results of our experiment on an Intel, 4-core system. We run omnetpp, a SPEC CPU 2006 benchmark along with another memory hog, whose memory intensity can be varied. This, in turn, lets us vary the rate at which the memory requests of omnetpp are serviced.
The x-axis shows the normalized request service rate of omnetpp, normalized to when it is run alone.
The y-axis shows the performance of omnetpp, normalized to when it is run alone.
As can be seen, there is a very strong, y=x like correlation between request service rate and performance.
We observe the same trend for various memory bound applications. Here are a couple of more examples.
Therefore, memory request service rate can be used as a proxy for performance.
Now, going back to the slowdown equation. We can replace performance by request service rate, based on our first observation, enabling us to express slowdown as the ratio of alone to shared request service rates.
Shared request service rate can be measured in a relatively straightforward manner when an application is run along with other applications.
Measuring alone request service rate, without actually running an application alone is harder. This is where our second observation comes into play.

## Slide 137: Key Observation 2
Request Service Rate Alone (RSRAlone) of an application can be estimated by giving the application highest priority in accessing memory
Highest priority  Little interference
(almost as if the application were run alone)
Notes: We observe that an application’s alone request service rate can be estimated by giving the application highest priority in accessing memory.
Because, when an application has highest priority, it receives little interference from other applications, almost as though the application were run alone.

## Slide 138: Key Observation 2
Request Buffer State
Main Memory
1. Run alone
Time units
Service order
Main Memory
1
2
Request Buffer State
Main Memory
2. Run with another application
Service order
Main Memory
1
2
3
Request Buffer State
Main Memory
3. Run with another application: highest priority
Service order
Main Memory
1
2
3
Time units
Time units
3
Notes: Here is an example.
An application, let’s call it the red application, is run by itself on a system. Two of its requests are queued at the memory controller request buffers. Since these are the only two requests queued up for main memory at this point, the memory controller schedules them back to back and they are serviced in two time units.
Now, the red application is run with another application, the blue application. The blue application’s request makes its way between two of the red application’s requests. A naïve memory scheduler could potentially schedule the requests in the order in which they arrived, delaying the red application’s second request by one time unit, as compared to when the application was run alone.
Next, let’s consider running the red and blue applications together, but give the red application highest priority. In this case, the memory scheduler schedules the two requests of the red application back to back, servicing them in two time units. Therefore, when the red application is given highest priority, its requests are serviced as though the application were run alone.

## Slide 139
Memory Interference-induced Slowdown Estimation (MISE) model for memory bound applications
Notes: Based on these two observations, our memory interference induced slowdown estimation (MISE) model for memory bound applications is as follows. Now, let’s analyze why this request service rate ratio based model holds for memory bound applications

## Slide 140: Key Observation 3
Memory-bound application
No interference
Compute Phase
Memory Phase
With interference
Memory phase slowdown dominates overall slowdown
time
time
Req
Req
Req
Req
Req
Req
Notes: A memory-bound application spends significant fraction of its execution time waiting for memory.
Let’s first look at the case when a memory-bound application is not receiving any interference.
The application does a small amount of compute at the core and then sends out a bunch of memory requests. The application cannot do any more compute until these requests are serviced.
Now, when this application experiences interference, the length of its compute phase does not change. However, the time taken to service the memory requests increases. In essence, since the application spends most of its time in the memory phase, the memory induced slowdown of the application dominates the overall slowdown of the application.

## Slide 141: Key Observation 3
Non-memory-bound application
time
time
No interference
Compute Phase
Memory Phase
With interference
Only memory fraction ( ) slows down with interference
Memory Interference-induced Slowdown Estimation (MISE) model for non-memory bound applications
Notes: However, this is not the case for a non-memory-bound application.
A non-memory-bound application spends a sizeable fraction of its time doing compute at the core and a smaller fraction of time waiting for memory. When the application experiences interference, the length of the compute phase does not change, whereas the memory phase slows down with interference.
Specifically, if alpha is the fraction of time the application spends in the memory phase, then 1 – alpha is the fraction of time it spends in the compute phase. The 1 – alpha fraction does not change with memory interference, however the alpha fraction slows down as the ratio of request service rate alone to request service rate shared.
We augment the MISE model to take this into account. Slowdown for non-memory-bound applications can be expressed as the sum of two quantities - 1 – alpha, the compute fraction that does not change with interference and the memory induced slowdown.

## Slide 142: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: Having discussed the key observations behind our MISE model, let me describe its implementation.

## Slide 143: Interval Based Operation
time
Interval
Estimate
slowdown
Interval
Estimate
slowdown
Measure RSRShared,
Estimate RSRAlone
Measure RSRShared,
Estimate RSRAlone
Notes: MISE operates on an interval basis.
Execution time is divided into intervals. During an interval, each application’s shared request service rate and alpha are measured.
And alone request service rate is estimated.
At the end of the interval, slowdown is estimated as a function of these three quantities.
This repeats during every interval.
Now, let us look at how each of these quantities is measured/estimated.

## Slide 144: Measuring RSRShared and α
Request Service Rate Shared (RSRShared)
  Per-core counter to track number of requests serviced
  At the end of each interval, measure
Memory Phase Fraction ( )
  Count number of stall cycles at the core
  Compute fraction of cycles stalled for memory
Notes: Shared request service rate can be measured using per-core counters to track the number of requests serviced during each interval.
At the end of the interval, SRSR can be computed as the number of requests serviced divided by the length of the interval.
Memory phase fraction of each application can be computed by counting the number of cycles the core stalls waiting for memory and then computing what fraction are these cycles of the interval length.
Measuring SRSR and alpha is the straightforward part. Now, for the more interesting part, estimating alone request service rate.

## Slide 145: Estimating Request Service Rate Alone (RSRAlone)
Divide each interval into shorter epochs
At the beginning of each epoch
  Memory controller randomly picks an application as the highest priority application
At the end of an interval, for each application, estimate
Goal: Estimate RSRAlone
How: Periodically give each application highest priority in accessing memory
Notes: Our goal is to estimate alone request service rate. To do this, we periodically give each application the highest priority in accessing memory, based on observation 2.
How exactly do we do this. First, each interval is divided into shorter epochs. At the beginning of each epoch, the memory controller picks one application at random and designates it the highest priority application. This way each application is given highest priority at different epochs during the interval.
At the end of the interval, ARSR is estimated for each application as the ratio of the number of requests of the application serviced during the high priority epochs to the number of cycles the application was given highest priority.
Now, is this an accurate way of estimating ARSR. It turns out not. We have been ignoring an inaccuracy all along.

## Slide 146: Inaccuracy in Estimating RSRAlone
Request Buffer
State
Main Memory
Time units
Service order
Main Memory
1
2
3
When an application has highest priority
  Still experiences some interference
Request Buffer
State
Main Memory
Time units
Service order
Main Memory
1
2
3
Time units
Service order
Main Memory
1
2
3
Interference Cycles
High Priority
Main Memory
Time units
Service order
Main Memory
1
2
3
Request Buffer
State
Notes: That is, even when an application has highest priority, it still experiences some interference from other applications.
Here is an example showing why.
The red application has highest priority and is run along with another application, the blue application. First, there is just one request in the request buffer and it is from the red application. Since this is the only request, it is scheduled by the memory controller and completes in one time unit.
While this request is being serviced, there comes another request from the blue application. Our memory controller is work conserving and schedules another application’s request, if there is no request from the red application. So, it schedules the blue application’s request next.
However, just as the blue application’s request is being scheduled comes another request from the red application. Ideally, we would like to pre-empt the blue application’s request. However, because of the way DRAM operates, preempting the blue application’s request incurs overhead. Therefore, the red application’s request would have to wait until the blue application’s request completes and only then is it serviced. These extra cycles that the red application spent waiting for the blue application’s request to complete are interference cycles that it would not have experienced had it been running alone.

## Slide 147: Accounting for Interference in RSRAlone Estimation
Solution: Determine and remove interference cycles from RSRAlone calculation
A cycle is an interference cycle if
  a request from the highest priority application is waiting in the request buffer and
  another application’s request was issued previously
Notes: The solution to account for this interference is to determine and remove such interference cycles from the ARSR computation.
How we do this is to subtract these cycles from the number of high priority epoch cycles.
Now, the question is how do we determine which cycles are interference cycles.
We deem a cycle an interference cycle if …. (read from slide)

## Slide 148: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: Having described the key observations behind our model and its implementation, we will put it all together

## Slide 149: MISE Model: Putting it All Together
time
Interval
Estimate
slowdown
Interval
Estimate
slowdown
Measure RSRShared,
Estimate RSRAlone
Measure RSRShared,
Estimate RSRAlone
Notes: MISE operates on an interval basis.
Execution time is divided into intervals. During an interval, each application’s shared request service rate and alpha are measured.
And alone request service rate is estimated.
At the end of the interval, slowdown is estimated as a function of these three quantities.
Now, let us look at how each of these quantities is measured/estimated.

## Slide 150: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: Now, having described the model and its implementation, let me present an evaluation of the model.

## Slide 151: Previous Work on Slowdown Estimation
Previous work on slowdown estimation
  STFM (Stall Time Fair Memory) Scheduling [Mutlu+, MICRO ‘07]
  FST (Fairness via Source Throttling) [Ebrahimi+, ASPLOS ‘10]
  Per-thread Cycle Accounting [Du Bois+, HiPEAC ‘13]
Basic Idea:
Hard
Easy
Count number of cycles application receives interference
Notes: The most relevant previous works on slowdown estimation are STFM, stall time fair memory scheduling and FST, fairness via source throttling.
FST employs similar mechanisms as STFM for memory-induced slowdown estimation, therefore, I will focus on STFM for the rest of the evaluation.
STFM estimates slowdown as the ratio of alone to shared stall times.
Stall time shared is easy to measure, analogous to shared request service rate
Stall time alone is harder and STFM estimates it by counting the number of cycles an application receives interference from other applications.

## Slide 152: Two Major Advantages of MISE Over STFM
Advantage 1:
  STFM estimates alone performance while an application is receiving interference  Hard
  MISE estimates alone performance while giving an application the highest priority  Easier
Advantage 2:
  STFM does not take into account compute phase for non-memory-bound applications
  MISE accounts for compute phase  Better accuracy
Notes: Let me now present the two major advantages of MISE over STFM, qualitatively.
First, STFM estimates alone performance of an application while it is receiving interference. This is hard because of BLP effects.
MISE addresses this difficulty by giving an application highest priority and then estimating its alone performance.
Second, STFM does not take into account compute phase for non-mem-bound applications. MISE accounts for compute phase and hence achieves better accuracy.

## Slide 153: Methodology
Configuration of our simulated system
  4 cores
  1 channel, 8 banks/channel
  DDR3 1066 DRAM
  512 KB private cache/core
Workloads
  SPEC CPU2006
  300 multi programmed workloads
Notes: Next, I will quantitatively compare MISE and STFM. Before that, let me present our methodology.
We carry out our evaluations on a 4-core, 1-channel DDR3 1066 DRAM system.
Our workloads are composed of SPEC CPU 2006 applications. We build 300 multiprogrammed workloads from these applications.

## Slide 154: Quantitative Comparison
Chart: Million Cycles
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
Actual | 2.7467 | 2.8146 | 2.981 | 2.6916 | 3.5156 | 2.4446 | 3.3601 | 3.2667 | 2.8783 | 2.9401 | 2.7229 | 2.9719 | 2.71 | 2.1736 | 2.0285 | 2.4098 | 2.0056 | 2.2585 | 2.1279 | 2.4625
STFM | 1.8517 | 1.9219 | 1.8786 | 1.8294 | 1.9487 | 1.8759 | 1.7936 | 1.7677 | 1.83 | 1.817 | 1.7232 | 1.7709 | 1.704 | 1.6746 | 1.6715 | 1.7352 | 1.6427 | 1.7084 | 1.6918 | 1.7477
MISE | 2.6655 | 2.8713 | 2.8244 | 2.6053 | 3.1741 | 2.6867 | 3.5471 | 3.4317 | 3.3 | 2.6747 | 2.8604 | 3.0821 | 2.8909 | 2.235 | 2.1161 | 2.3639 | 1.999 | 2.0667 | 2.1632 | 2.3161
SPEC CPU 2006 application
leslie3d
Notes: This graph shows the actual slowdown of leslie3d, a memory-bound application, with time (in million cycles).
Here are slowdown estimates from STFM and here are slowdown estimates from MISE. As can be seen, MISE’s slowdown estimates are much closer to the actual slowdowns. This is because MISE estimates leslie’s alone performance while giving it highest priority, whereas STFM tries to estimate it while leslie receives interference from other applications.

## Slide 155: Comparison to STFM
cactusADM
Chart: Slowdown
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
Actual | 1.495 | 1.5295 | 1.6709 | 1.5475 | 1.6605 | 1.5731 | 1.9783 | 1.7095 | 1.5337 | 1.5256 | 1.4754 | 1.5235 | 1.5214 | 1.7913 | 1.6855 | 1.6301 | 1.5933 | 1.6732 | 1.5495 | 1.6973
STFM | 1.25 | 1.3555 | 1.3435 | 1.3721 | 1.3293 | 1.3149 | 1.2341 | 1.3128 | 1.3228 | 1.3579 | 1.3509 | 1.344 | 1.4008 | 1.3967 | 1.5397 | 1.5867 | 1.5517 | 1.5683 | 1.5638 | 1.3614
MISE | 1.5723 | 1.5685 | 1.6897 | 1.5829 | 1.73 | 1.6866 | 2.1706 | 1.8114 | 1.5947 | 1.5898 | 1.5347 | 1.5537 | 1.6001 | 1.8673 | 1.7348 | 1.6758 | 1.6313 | 1.7322 | 1.6362 | 1.7298
Chart: Slowdown
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
Actual | 1.7536 | 1.697 | 1.8734 | 1.7248 | 1.9225 | 1.6413 | 1.9296 | 2.1339 | 2.0504 | 1.9754 | 1.8732 | 2.1705 | 2.0085 | 2.239 | 2.2425 | 2.2469 | 1.9042 | 2.3715 | 2.0927 | 2.5902
STFM | 1.3661 | 1.3843 | 1.3635 | 1.3908 | 1.3589 | 1.35 | 1.3746 | 1.5894 | 1.5811 | 1.5995 | 1.5987 | 1.5832 | 1.5771 | 2.0246 | 1.9878 | 1.9883 | 1.9797 | 1.9406 | 1.9709 | 1.9629
MISE | 1.8607 | 1.9645 | 1.9765 | 1.8835 | 2.5202 | 1.8326 | 2.2231 | 2.3347 | 2.178 | 2.097 | 2.1736 | 2.1054 | 2.0591 | 2.3181 | 2.2502 | 2.3946 | 2.1703 | 2.5387 | 2.2735 | 2.6647
GemsFDTD
Chart: Slowdown
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
Actual | 1.9414 | 2.1412 | 2.406 | 2.0632 | 2.7223 | 2.6572 | 3.1068 | 3.1879 | 2.6035 | 2.4937 | 2.4704 | 2.8774 | 2.6478 | 2.6947 | 2.7804 | 2.9653 | 2.8228 | 2.5796 | 2.6027 | 2.7846
STFM | 1.5023 | 1.4705 | 1.8931 | 1.4971 | 1.6676 | 1.6306 | 1.8055 | 1.7004 | 1.5827 | 1.7021 | 1.7571 | 1.8054 | 1.974 | 2.2827 | 2.3098 | 2.107 | 1.6316 | 2.0168 | 2.0447 | 2.0375
MISE | 1.916 | 2.3469 | 2.5021 | 2.481 | 2.7434 | 2.413 | 3.2611 | 3.5557 | 2.6948 | 2.6542 | 3.0171 | 2.4489 | 2.5681 | 2.7574 | 3.1405 | 3.0343 | 2.527 | 2.8438 | 3.1033 | 3.2769
soplex
Chart: Slowdown
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
Actual | 1.0179 | 1.0228 | 1.5311 | 1.2016 | 1.0185 | 1.0121 | 1.0059 | 1.0071 | 1.1261 | 1.5714 | 1.0808 | 1.0167 | 1.0097 | 1.2303 | 1.0956 | 1.0308 | 1.0187 | 1.3242 | 1.3257 | 1.0134
STFM | 2.6564 | 2.8136 | 2.323 | 1.9913 | 2.1243 | 2.8472 | 2.9844 | 2.4594 | 2.5397 | 2.2388 | 3.0174 | 2.8437 | 3.3951 | 3.9402 | 2.5308 | 2.8686 | 3.3191 | 2.5052 | 2.3033 | 2.0445
MISE | 1.0005 | 1.0032 | 1.7563 | 1.0691 | 0.99707 | 1.0011 | 1.0016 | 0.99869 | 1.0593 | 1.3748 | 1.0555 | 1.0003 | 1.0006 | 1.0639 | 1.0105 | 0.98886 | 1.0009 | 0.9221 | 1.0907 | 1.0039
wrf
Chart: Slowdown
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
Actual | 1.0394 | 1.0432 | 1.0258 | 1.0358 | 1.031 | 1.0316 | 1.0304 | 1.0232 | 1.0226 | 1.0158 | 1.0543 | 1.0328 | 1.0751 | 1.0632 | 1.0517 | 1.053 | 1.029 | 1.0322 | 1.031 | 1.0246
STFM | 2.1276 | 2.0414 | 1.9127 | 1.8201 | 2.3708 | 1.9609 | 1.9559 | 2.062 | 2.2477 | 2.173 | 3.9673 | 2.3084 | 2.4138 | 2.5477 | 2.8093 | 2.6087 | 2.1795 | 1.9627 | 1.8871 | 2.0011
MISE | 1.0191 | 1.0068 | 1.0168 | 0.98223 | 1.031 | 0.96844 | 1.0017 | 1.0177 | 0.99417 | 1.0091 | 1.0383 | 1.0293 | 1.0276 | 1.0128 | 1.0242 | 1.0231 | 0.99687 | 1.0223 | 0.89507 | 1.0191
calculix
Chart: Slowdown
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
Actual | 1.0008 | 1.0011 | 1.0029 | 1.0014 | 1.0016 | 1.0015 | 1.0038 | 1.0016 | 1.0011 | 1.0034 | 1.0391 | 1.1297 | 1.0014 | 1.0018 | 1.0019 | 1.002 | 1.0012 | 1.0008 | 1.0011 | 1.0012
STFM | 2.5587 | 2.6401 | 2.5897 | 1.8924 | 2.9635 | 3.1523 | 2.659 | 2.2124 | 3.2205 | 2.9929 | 3.5898 | 2.7107 | 2.1336 | 3.0915 | 3.0289 | 3.0638 | 3.0873 | 2.3554 | 2.7464 | 2.2834
MISE | 1.0002 | 1.0002 | 1.0015 | 1.0003 | 1.0007 | 0.99984 | 1.0012 | 0.99949 | 0.99671 | 1.0015 | 0.99044 | 0.86466 | 1.0003 | 1.0004 | 1.0006 | 0.99474 | 0.99903 | 0.99882 | 1.0001 | 1.0004
povray
Average error of MISE: 8.2%
Average error of STFM: 29.4%
(across 300 workloads)
Notes: Several more applications. For most applications, MISE’s slowdown estimates are more accurate.
On average, MISE’s error is 8.2%, while STFM’s error is 29.4%, across our 300 workloads.

## Slide 156: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: I have described our MISE model to estimate application slowdowns. Now, once we have slowdown estimates from our model, we can leverage them to control slowdowns. Let me present our first mechanism to control slowdowns – providing soft slowdown guarantees.

## Slide 157: Providing “Soft” Slowdown Guarantees
Goal
  1. Ensure QoS-critical applications meet a prescribed slowdown bound
  2. Maximize system performance for other applications
Basic Idea
  Allocate just enough bandwidth to QoS-critical application
  Assign remaining bandwidth to other applications
Notes: The goal of this mechanism is to .. <read off slide>.
The basic idea is to allocate just enough bandwidth the QoS-critical application, while assigning the remaining bandwidth among the other applications.

## Slide 158: MISE-QoS: Mechanism to Provide Soft QoS
Assign an initial bandwidth allocation to QoS-critical application
Estimate slowdown of QoS-critical application using the MISE model
After every N intervals
  If slowdown > bound B +/- ε, increase bandwidth allocation
  If slowdown < bound B +/- ε, decrease bandwidth allocation
When slowdown bound not met for N intervals
  Notify the OS so it can migrate/de-schedule jobs
Notes: SLIDE NEEDS WORK

## Slide 159: Methodology
Each application (25 applications in total) considered the QoS-critical application
Run with 12 sets of co-runners of different memory intensities
Total of 300 multiprogrammed workloads
Each workload run with 10 slowdown bound values
Baseline memory scheduling mechanism
  Always prioritize QoS-critical application
  [Iyer+, SIGMETRICS 2007]
  Other applications’ requests scheduled in FRFCFS order
  [Zuravleff +, US Patent 1997, Rixner+, ISCA 2000]
Notes: Read off slide

## Slide 160: A Look at One Workload
Chart: Slowdown
| leslie3d | hmmer | lbm | omnetpp
AlwaysPrioritize | 1.9301 | 2.511 | 2.8159 | 2.7346
MISE-QoS-10/1 | 2.8374 | 2.2769 | 2.0523 | 2.0142
MISE-QoS-10/3 | 2.6976 | 2.3196 | 2.1221 | 2.084
MISE-QoS-10/5 | 2.0128 | 2.5056 | 2.6593 | 2.5534
MISE-QoS-10/7 | 1.9063 | 2.508 | 2.8014 | 2.6609
MISE-QoS-10/9 | 1.9063 | 2.508 | 2.8014 | 2.6609
QoS-critical
non-QoS-critical
MISE is effective in
meeting the slowdown bound for the QoS-critical application
improving performance of non-QoS-critical applications
Slowdown Bound = 10
Slowdown Bound = 3.33
Slowdown Bound = 2

## Slide 161: Effectiveness of MISE in Enforcing QoS
 | Predicted Met | Predicted Not Met
QoS Bound Met | 78.8% | 2.1%
QoS Bound Not Met | 2.2% | 16.9%
Across 3000 data points
MISE-QoS meets the bound for 80.9% of workloads
AlwaysPrioritize meets the bound for 83% of workloads
MISE-QoS correctly predicts whether or not
the bound is met for 95.7% of workloads

## Slide 162: Performance of Non-QoS-Critical Applications
Chart: Number of Memory Intensive Applications
| 0 | 1 | 2 | 3 | Avg
AlwaysPrioritize | 1.2932 | 0.92684 | 0.63783 | 0.47247 | 0.83259
MISE-QoS-10/1 | 1.3105 | 1.0515 | 0.75708 | 0.556 | 0.91875
MISE-QoS-10/3 | 1.3105 | 1.0471 | 0.75276 | 0.54982 | 0.91504
MISE-QoS-10/5 | 1.3104 | 1.0268 | 0.71476 | 0.51722 | 0.89229
MISE-QoS-10/7 | 1.3101 | 0.96233 | 0.65406 | 0.47556 | 0.85051
MISE-QoS-10/9 | 1.2966 | 0.92898 | 0.64287 | 0.47149 | 0.83499
Higher performance when bound is loose
When slowdown bound is 10/3
MISE-QoS improves system performance by 10%

## Slide 163: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown

## Slide 164: Other Results in the Paper
Sensitivity to model parameters
  Robust across different values of model parameters
Comparison of STFM and MISE models in enforcing soft slowdown guarantees
  MISE significantly more effective in enforcing guarantees
Minimizing maximum slowdown
  MISE improves fairness across several system configurations

## Slide 165: Summary
Uncontrolled memory interference slows down applications unpredictably
Goal: Estimate and control slowdowns
Key contribution
  MISE: An accurate slowdown estimation model
  Average error of MISE: 8.2%
Key Idea
  Request Service Rate is a proxy for performance
  Request Service Rate Alone estimated by giving an application highest priority in accessing memory
Leverage slowdown estimates to control slowdowns
  Providing soft slowdown guarantees
  Minimizing maximum slowdown

## Slide 166: MISE: Pros and Cons
Upsides:
  Simple new insight to estimate slowdown
  Much more accurate slowdown estimations than prior techniques (STFM, FST)
  Enables a number of QoS mechanisms that can use slowdown estimates to satisfy performance requirements
Downsides:
  Slowdown estimation is not perfect - there are still errors
  Does not take into account caches and other shared resources in slowdown estimation

## Slide 167: More on MISE
Lavanya Subramanian, Vivek Seshadri, Yoongu Kim, Ben Jaiyen, and Onur Mutlu, "MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA), Shenzhen, China, February 2013. Slides (pptx)

## Slide 168: Extending MISE to Shared Caches: ASM
Lavanya Subramanian, Vivek Seshadri, Arnab Ghosh, Samira Khan, and Onur Mutlu, "The Application Slowdown Model: Quantifying and Controlling the Impact of Inter-Application Interference at Shared Caches and Main Memory" Proceedings of the 48th International Symposium on Microarchitecture (MICRO), Waikiki, Hawaii, USA, December 2015. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Source Code]

## Slide 169: Handling Memory Interference In Multithreaded Applications
Eiman Ebrahimi, Rustam Miftakhutdinov, Chris Fallin,
Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Parallel Application Memory Scheduling" Proceedings of the 44th International Symposium on Microarchitecture (MICRO),
Porto Alegre, Brazil, December 2011. Slides (pptx)

## Slide 170: Multithreaded (Parallel) Applications
Threads in a multi-threaded application can be inter-dependent
  As opposed to threads from different applications
Such threads can synchronize with each other
  Locks, barriers, pipeline stages, condition variables, semaphores, …
Some threads can be on the critical path of execution due to synchronization; some threads are not
Even within a thread, some “code segments” may be on the critical path of execution; some are not

## Slide 171: Critical Sections
Enforce mutually exclusive access to shared data
Only one thread can be executing it at a time
Contended critical sections make threads wait  threads causing serialization can be on the critical path
Each thread:
loop {
Compute
lock(A)
Update shared data
unlock(A)
}
N
C

## Slide 172: Barriers
Synchronization point
Threads have to wait until all threads reach the barrier
Last thread arriving at the barrier is on the critical path
Each thread:
loop1 {
Compute
}
barrier
loop2 {
Compute
}

## Slide 173: Stages of Pipelined Programs
Loop iterations are statically divided into code segments called stages
Threads execute stages on different cores
Thread executing the slowest stage is on the critical path
loop {
Compute1
Compute2
Compute3
}
A
B
C
A
B
C

## Slide 174: Handling Interference in Parallel Applications
Threads in a multithreaded application are inter-dependent
Some threads can be on the critical path of execution due to synchronization; some threads are not
How do we schedule requests of inter-dependent threads to maximize multithreaded application performance?
  Idea: Estimate limiter threads likely to be on the critical path and prioritize their requests; shuffle priorities of non-limiter threads to reduce memory interference among them [Ebrahimi+, MICRO’11]
  Hardware/software cooperative limiter thread estimation:
    Thread executing the most contended critical section
    Thread executing the slowest pipeline stage
    Thread that is falling behind the most in reaching a barrier
PAMS Micro 2011 Talk

## Slide 175: Prioritizing Requests from Limiter Threads
175
Critical Section 1
Barrier
Non-Critical Section
Waiting for Sync or Lock
Thread D
Thread C
Thread B
Thread A
Time
Barrier
Time
Barrier
Thread D
Thread C
Thread B
Thread A
Critical Section 2
Critical Path
Saved Cycles
Limiter Thread:
D
B
C
A
Most Contended Critical Section:
1
Limiter Thread Identification

## Slide 176: Parallel App Mem Scheduling: Pros and Cons
Upsides:
  Improves the performance of multi-threaded applications
  Provides a mechanism for estimating “limiter threads”
  Opens a path for slowdown estimation for multi-threaded applications
Downsides:
  What if there are multiple multi-threaded applications running together?
  Limiter thread estimation can become complex

## Slide 177: More on PAMS
Eiman Ebrahimi, Rustam Miftakhutdinov, Chris Fallin, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Parallel Application Memory Scheduling" Proceedings of the 44th International Symposium on Microarchitecture (MICRO), Porto Alegre, Brazil, December 2011. Slides (pptx)

## Slide 178: Other Ways of Handling Memory Interference

## Slide 179: Fundamental Interference Control Techniques
Goal: to reduce/control inter-thread memory interference
1. Prioritization or request scheduling
2. Data mapping to banks/channels/ranks
3. Core/source throttling
4. Application/thread scheduling

## Slide 180: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers
  QoS-aware interconnects
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system
  QoS-aware data mapping to memory controllers
  QoS-aware thread scheduling to cores

## Slide 181: Memory Channel Partitioning
Sai Prashanth Muralidhara, Lavanya Subramanian, Onur Mutlu, Mahmut Kandemir, and Thomas Moscibroda, "Reducing Memory Interference in Multicore Systems via
Application-Aware Memory Channel Partitioning” 44th International Symposium on Microarchitecture (MICRO),
Porto Alegre, Brazil, December 2011. Slides (pptx)
MCP Micro 2011 Talk

## Slide 182: Observation: Modern Systems Have Multiple Channels
A new degree of freedom
Mapping data across multiple channels
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 183: Data Mapping in Current Systems
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory
Causes interference between applications’ requests
Page
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 184: Partitioning Channels Between Applications
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory
Page
Eliminates interference between applications’ requests
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 185: Overview: Memory Channel Partitioning (MCP)
Goal
  Eliminate harmful interference between applications
Basic Idea
  Map the data of badly-interfering applications to different channels
Key Principles
  Separate low and high memory-intensity applications
  Separate low and high row-buffer locality applications
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 186: Key Insight 1: Separate by Memory Intensity
High memory-intensity applications interfere with low memory-intensity applications in shared memory channels
Map data of low and high memory-intensity applications
to different channels
1
2
3
4
5
Channel 0
Bank 1
Channel 1
Bank 0
Conventional Page Mapping
Red App
Blue App
Time Units
Core
Core
Bank 1
Bank 0
Channel Partitioning
Red App
Blue App
Channel 0
Time Units
1
2
3
4
5
Channel 1
Core
Core
Bank 1
Bank 0
Bank 1
Bank 0
Saved Cycles
Saved Cycles

## Slide 187: Key Insight 2: Separate by Row-Buffer Locality
High row-buffer locality applications interfere with low
row-buffer locality applications in shared memory channels
Conventional Page Mapping
Channel 0
Bank 1
Channel 1
Bank 0
R1
R0
R2
R3
R0
R4
Request Buffer State
Bank 1
Bank 0
Channel 1
Channel 0
R0
R0
Service Order
1
2
3
4
5
6
R2
R3
R4
R1
Time units
Bank 1
Bank 0
Bank 1
Bank 0
Channel 1
Channel 0
R0
R0
Service Order
1
2
3
4
5
6
R2
R3
R4
R1
Time units
Bank 1
Bank 0
Bank 1
Bank 0
R0
Channel 0
R1
R2
R3
R0
R4
Request Buffer State
Channel Partitioning
Bank 1
Bank 0
Bank 1
Bank 0
Channel 1
Saved
Cycles
Map data of low and high row-buffer locality applications to different channels

## Slide 188: Memory Channel Partitioning (MCP) Mechanism
1. Profile applications
2. Classify applications into groups
3. Partition channels between application groups
4. Assign a preferred channel to each application
5. Allocate application pages to preferred channel
Hardware
System Software
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 189: Interval Based Operation
time
Current Interval
Next Interval
1. Profile applications
2. Classify applications into groups
3. Partition channels between groups
4. Assign preferred channel to applications
5. Enforce channel preferences

## Slide 190: Observations
Applications with very low memory-intensity rarely access memory  Dedicating channels to them results in precious memory bandwidth waste
They have the most potential to keep their cores busy  We would really like to prioritize them
They interfere minimally with other applications  Prioritizing them does not hurt others

## Slide 191: Integrated Memory Partitioning and Scheduling (IMPS)
Always prioritize very low memory-intensity applications in the memory scheduler
Use memory channel partitioning to mitigate interference between other applications
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 192: Hardware Cost
Memory Channel Partitioning (MCP)
  Only profiling counters in hardware
  No modifications to memory scheduling logic
  1.5 KB storage cost for a 24-core, 4-channel system
Integrated Memory Partitioning and Scheduling (IMPS)
  A single bit per request
  Scheduler prioritizes based on this single bit
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 193: Performance of Channel Partitioning
1%
5%
Chart: Normalized System Performance
|
FRFCFS | 1
ATLAS | 1.012
TCM | 1.061
MCP | 1.071
IMPS | 1.1108
7%
11%
Better system performance than the best previous scheduler
at lower hardware cost
Averaged over 240 workloads

## Slide 194: Combining Multiple Interference Control Techniques
Combined interference control techniques can mitigate interference much more than a single technique alone can do
The key challenge is:
  Deciding what technique to apply when
  Partitioning work appropriately between software and hardware

## Slide 195: MCP and IMPS: Pros and Cons
Upsides:
  Keeps the memory scheduling hardware simple
  Combines multiple interference reduction techniques
  Can provide performance isolation across applications mapped to different channels
  General idea of partitioning can be extended to smaller granularities in the memory hierarchy: banks, subarrays, etc.
Downsides:
  Reacting is difficult if workload changes behavior after profiling
  Overhead of moving pages between channels restricts benefits

## Slide 196: More on Memory Channel Partitioning
Sai Prashanth Muralidhara, Lavanya Subramanian, Onur Mutlu, Mahmut Kandemir, and Thomas Moscibroda, "Reducing Memory Interference in Multicore Systems via Application-Aware Memory Channel Partitioning" Proceedings of the 44th International Symposium on Microarchitecture (MICRO), Porto Alegre, Brazil, December 2011. Slides (pptx)

## Slide 197: Fundamental Interference Control Techniques
Goal: to reduce/control inter-thread memory interference
1. Prioritization or request scheduling
2. Data mapping to banks/channels/ranks
3. Core/source throttling
4. Application/thread scheduling

## Slide 198: Fairness via Source Throttling
Eiman Ebrahimi, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Fairness via Source Throttling: A Configurable and High-Performance
Fairness Substrate for Multi-Core Memory Systems" 15th Intl. Conf. on Architectural Support for Programming Languages and Operating Systems (ASPLOS),
pages 335-346, Pittsburgh, PA, March 2010. Slides (pdf)
FST ASPLOS 2010 Talk

## Slide 199: Many Shared Resources
Core 0
Core 1
Core 2
Core N
Shared Cache
Memory Controller
DRAM
Bank 0
DRAM
Bank 1
DRAM Bank 2
...
DRAM Bank K
...
Shared Memory
Resources
Chip Boundary
On-chip
Off-chip
199

## Slide 200: The Problem with “Smart Resources”
Independent interference control mechanisms in caches, interconnect, and memory can contradict each other
Explicitly coordinating mechanisms for different resources requires complex implementation
How do we enable fair sharing of the entire memory system by controlling interference in a coordinated manner?

## Slide 201: Source Throttling: A Fairness Substrate
Key idea: Manage inter-thread interference at the cores (sources), not at the shared resources
Dynamically estimate unfairness in the memory system
Feed back this information into a controller
Throttle cores’ memory access rates accordingly
  Whom to throttle and by how much depends on performance target (throughput, fairness, per-thread QoS, etc)
  E.g., if unfairness > system-software-specified target then throttle down core causing unfairness & throttle up core that was unfairly treated
Ebrahimi et al., “Fairness via Source Throttling,” ASPLOS’10, TOCS’12.

## Slide 202: Fairness via Source Throttling (FST)
Two components (interval-based)
Run-time unfairness evaluation (in hardware)
  Dynamically estimates the unfairness (application slowdowns) in the memory system
  Estimates which application is slowing down which other
Dynamic request throttling (hardware or software)
  Adjusts how aggressively each core makes requests to the shared resources
  Throttles down request rates of cores causing unfairness
    Limit miss buffers, limit injection rate

## Slide 203: Fairness via Source Throttling (FST) [ASPLOS’10]
203
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
(limit injection rate and parallelism)
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering
⎪
⎨
⎪
⎧
⎩
Slowdown Estimation
Time
Interval 1
Interval 2
Interval 3
Runtime Unfairness
Evaluation
Dynamic
Request Throttling

## Slide 204: Dynamic Request Throttling
Goal: Adjust how aggressively each core makes requests to the shared memory system
Mechanisms:
  Miss Status Holding Register (MSHR) quota
    Controls the number of concurrent requests accessing shared resources from each application
  Request injection frequency
    Controls how often memory requests are issued to the last level cache from the MSHRs

## Slide 205: Dynamic Request Throttling
Throttling level assigned to each core determines both MSHR quota and request injection rate
Throttling level | MSHR quota | Request Injection Rate
100% | 128 | Every cycle
50% | 64 | Every other cycle
25% | 32 | Once every 4 cycles
10% | 12 | Once every 10 cycles
5% | 6 | Once every 20 cycles
4% | 5 | Once every 25 cycles
3% | 3 | Once every 30 cycles
2% | 2 | Once every 50 cycles
Total # of
MSHRs: 128

## Slide 206: System Software Support
Different fairness objectives can be configured by system software
  Keep maximum slowdown in check
    Estimated Max Slowdown < Target Max Slowdown
  Keep slowdown of particular applications in check to achieve a particular performance target
    Estimated Slowdown(i) < Target Slowdown(i)
Support for thread priorities
  Weighted Slowdown(i) = Estimated Slowdown(i) x Weight(i)

## Slide 207: Source Throttling Results: Takeaways
Source throttling alone provides better performance than a combination of “smart” memory scheduling and fair caching
  Decisions made at the memory scheduler and the cache sometimes contradict each other
Neither source throttling alone nor “smart resources” alone provides the best performance
Combined approaches are even more powerful
  Source throttling and resource-based interference control

## Slide 208: Source Throttling: Ups and Downs
Advantages
  + Core/request throttling is easy to implement: no need to change the memory scheduling algorithm
  + Can be a general way of handling shared resource contention
  + Can reduce overall load/contention in the memory system
Disadvantages
  - Requires slowdown estimations  difficult to estimate
  - Thresholds can become difficult to optimize
   throughput loss due to too much throttling
   can be difficult to find an overall-good configuration

## Slide 209: More on Source Throttling (I)
Eiman Ebrahimi, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Fairness via Source Throttling: A Configurable and High-Performance Fairness Substrate for Multi-Core Memory Systems" Proceedings of the 15th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), pages 335-346, Pittsburgh, PA, March 2010. Slides (pdf)

## Slide 210: More on Source Throttling (II)
Kevin Chang, Rachata Ausavarungnirun, Chris Fallin, and Onur Mutlu, "HAT: Heterogeneous Adaptive Throttling for On-Chip Networks" Proceedings of the 24th International Symposium on Computer Architecture and High Performance Computing (SBAC-PAD), New York, NY, October 2012. Slides (pptx) (pdf)

## Slide 211: More on Source Throttling (III)
George Nychis, Chris Fallin, Thomas Moscibroda, Onur Mutlu, and Srinivasan Seshan, "On-Chip Networks from a Networking Perspective: Congestion and Scalability in Many-core Interconnects" Proceedings of the 2012 ACM SIGCOMM Conference (SIGCOMM), Helsinki, Finland, August 2012. Slides (pptx)

## Slide 212: Fundamental Interference Control Techniques
Goal: to reduce/control interference
1. Prioritization or request scheduling
2. Data mapping to banks/channels/ranks
3. Core/source throttling
4. Application/thread scheduling
Idea: Pick threads that do not badly interfere with each other to be scheduled together on cores sharing the memory system

## Slide 213: Application-to-Core Mapping to Reduce Interference
Reetuparna Das, Rachata Ausavarungnirun, Onur Mutlu, Akhilesh Kumar, and Mani Azimi, "Application-to-Core Mapping Policies to Reduce Memory System Interference in Multi-Core Systems" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA), Shenzhen, China, February 2013. Slides (pptx)
Key ideas:
  Cluster threads to memory controllers (to reduce across chip interference)
  Isolate interference-sensitive (low-intensity) applications in a separate cluster (to reduce interference from high-intensity applications)
  Place applications that benefit from memory bandwidth closer to the controller

## Slide 214: Multi-Core to Many-Core
Multi-Core
Many-Core
Notes: Processor industry has adopted multi-cores a power-efficient way for throughput scaling
Today as processors move from few cores to few hundred cores we face several new challenges

## Slide 215: Many-Core On-Chip Communication
Memory
Controller
Shared
Cache Bank
$
$
Light
Heavy
Applications
Notes: In a many-core processor with several hundred cores communication plays a key role in system design
I show an example of on-chip communication
An application generates requests to memory sub-system which can be either satisfied by caches or have to go all the way to main memory via memory controllers
Some applications may generate few requests and are light and some may generate lots of requests and thus heavy

## Slide 216: Problem: Spatial Task Scheduling
Applications
Cores
How to map applications to cores?
Notes: In this paper we try to solve the problem of spatial task scheduling
For spatial scheduling there will be lots of applications with diverse characteristics and there will be lots of cores
The key question is how to map these applications to cores to maximize performance fairness and energy efficiency

## Slide 217: Challenges in Spatial Task Scheduling
Applications
Cores
How to reduce destructive interference between applications?
How to reduce communication distance?
How to prioritize applications to improve throughput?
Notes: When doing the application to core mapping we need to answer several questions –
The first obvious question is how do we reduce the distance that your requests travel
Then how do you ensure that requests generated by two different applications donot destructively interfere with each other and degrade the overall performance
Finally if we have applications which are very sensitive to memory system performance how do you prioritize them and still ensure good fairness and load balance

## Slide 218: Application-to-Core Mapping
Balancing
Isolation
Radial Mapping
Clustering
Improve Locality
Reduce Interference
Improve Bandwidth
Utilization
Reduce Interference
Improve Bandwidth
Utilization
Notes: We take four steps to a2c
First we adopt clustering for improving locality and reducing interference
Then we balance the load across the clusters
Next we ensure to isolate sensitive applications such they suffer minimal interference
Finally we schedule critical application close to shared memory system resources

## Slide 219: Step 1 — Clustering
Inefficient data mapping to memory and caches
Memory
Controller
Notes: In a naive scheduler the requests generated by your application could go to all corners of a chip
How do you clustering the data so that requests generated by an application are satisfied by the resources within a cluster

## Slide 220: Step 1 — Clustering
Improved Locality
Reduced Interference
Cluster 0
Cluster 2
Cluster 1
Cluster 3
Notes: If you could somehow make sure to map the data to the resources within a cluster then there are two benefirs first you can improve communication locality second you can also reduce the interference between requests generated by different applications
Say first divide the chip into clusters

## Slide 221: System Performance
Chart: Normalized Weighted Speedup
| MPKI500 | MPKI1000 | MPKI1500 | MPKI2000 | Avg
BASE | 1 | 1 | 1 | 1 | 1
BASE+CLS | 1.0372 | 1.1184 | 1.1114 | 1.1307 | 1.0935
A2C | 1.0655 | 1.2016 | 1.2154 | 1.2299 | 1.1672
System performance improves by 17%
Notes: Radial mapping was consistently beneficial for all workloads

## Slide 222: Network Power
Chart: Normalized NoC Power
| MPKI500 | MPKI1000 | MPKI1500 | MPKI2000 | Avg
BASE | 1 | 1 | 1 | 1 | 1
BASE+CLS | 0.71297 | 0.70762 | 0.68333 | 0.68711 | 0.6911
A2C | 0.39619 | 0.50039 | 0.49336 | 0.49562 | 0.47611
Average network power consumption reduces by 52%

## Slide 223: More on App-to-Core Mapping
Reetuparna Das, Rachata Ausavarungnirun, Onur Mutlu, Akhilesh Kumar, and Mani Azimi, "Application-to-Core Mapping Policies to Reduce Memory System Interference in Multi-Core Systems" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA), Shenzhen, China, February 2013. Slides (pptx)

## Slide 224: Interference-Aware Thread Scheduling
An example from scheduling in compute clusters (data centers)
Data centers can be running virtual machines

## Slide 225: Virtualized Cluster
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
How to dynamically schedule VMs onto hosts?
Distributed Resource Management (DRM) policies
Notes: In a virtualized cluster, we have a set of physical hosts, and many virtual machines.
One key question to manage the virtualized cluster is how to dynamic scheduling the virtual machines onto the physical hosts?
To achieve high resource utilization and energy savings, virtualized systems usually employ distributed resource management (DRM) policies to solve this problem.

## Slide 226: Conventional DRM Policies
Core0
Core1
Host
LLC
DRAM
App
App
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
VM
App
Memory Capacity
CPU
Based on operating-system-level metrics
e.g., CPU utilization, memory capacity demand
Notes: Could will map them in this manner.
Conventional DRM policies, usually make the mapping decision based on operating-system level metrics, such as CPU utilization, memory capacity, and fit the virtual machines into physical hosts dynamically.
Here is an example, let’s use the height to indicate the CPU utilization and the width to indicate the memory capacity demand. If we have four virtual machines like this, we can fit them into the two hosts.

## Slide 227: Microarchitecture-level Interference
VM
App
Core0
Core1
Host
LLC
DRAM
VM
App
VMs within a host compete for:
  Shared cache capacity
  Shared memory bandwidth
Can operating-system-level metrics capture the microarchitecture-level resource interference?
Notes: However, another key aspect that impact the virtual machines performance is the microarchitecture-level interference.
Virtual machines within a host compete at:
1) …
VMs will evict each other’s data from the last level cache, causing an increase in memory access latency, thus resulting in performance degradation.
2) …
VMs’ memory requests also contend at the different components of main memory, such as channels, ranks, and banks. Also resulting in performance degradation.
One question raised here is: can the operating-system-level metrics reflect the micro-architecture-level resources interference?

## Slide 228: Microarchitecture Unawareness
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
VM | Operating-system-level metrics | 
 | CPU Utilization | Memory Capacity
 | 92% | 369 MB
 | 93% | 348 MB
App
App
STREAM
gromacs
Microarchitecture-level metrics | 
LLC Hit Ratio | Memory Bandwidth
2% | 2267 MB/s
98% | 1 MB/s
VM
App
Memory Capacity
CPU
Notes: Could possibly map VM to Host in this manner. NO topology
Starved.
We profiled many benchmarks and found many of them exhibit the similar CPU utilization and memory capacity demand. Take the STREAM and gromacs for example, their cpu utilization and memory capacity demand are similar.
If we use conventional DRM to schedule them, this is a possible mapping. The two STREAM running on the same host.
However, although the cpu and memory usage are similar, the microarchitecture-level resource are totally different. STREAM…
Gromacs …
Thus in this mapping, this host may already experiencing heavily contention.

## Slide 229: Impact on Performance
Chart: IPC (Harmonic Mean)
| IPC (Harmonic Mean)
Conventional DRM | 0.30788
with Microarchitecture Awareness | 0.45937
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
App
STREAM
gromacs
VM
App
Memory Capacity
CPU
SWAP
Notes: Although the conventional DRM policies now aware of microarchitecture level contention, how much benefit will we get if we considering them?
We did an experiment use the STREAM and groamcs benchmark. When two STREAM are locate on the same host, the harmonic mean of IPC across all the VMs are 0.30.

## Slide 230: Impact on Performance
Chart: IPC (Harmonic Mean)
| IPC (Harmonic Mean)
Conventional DRM | 0.30788
with Microarchitecture Awareness | 0.45937
49%
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
App
STREAM
gromacs
VM
App
Memory Capacity
CPU
We need microarchitecture-level interference awareness in DRM!
Notes: However, after we migrate STREAM to the other host and migrate gromacs back. The performance is improved by nearly fifty percentage.
Which indicate that we need microarchitecture-level interference awareness in distributed resource management.

## Slide 231: A-DRM: Architecture-aware DRM
Goal: Take into account microarchitecture-level shared resource interference
  Shared cache capacity
  Shared memory bandwidth
Key Idea:
  Monitor and detect microarchitecture-level shared resource interference
  Balance microarchitecture-level resource usage across cluster to minimize memory interference while maximizing system performance
Notes: A-DRM takes into account two main sources of interference at the microarchitecture-level,
shared last level cache capacity and
memory bandwidth.
The key idea of A-DRM is to monitors the microarchitecture-level resource usage, and balance it across the cluster.

## Slide 232: A-DRM: Architecture-aware DRM
OS+Hypervisor
VM
App
VM
App
A-DRM: Global Architecture –aware Resource Manager
Profiling Engine
Architecture-aware
Interference Detector
Architecture-aware
Distributed Resource Management (Policy)
Migration Engine
Hosts
Controller
CPU/Memory Capacity
Profiler
Architectural Resource
•••
Architectural Resources
Notes: In addition to conventional DRM, A-DRM add
1) an architectural resource profiler at each host
We add two … to the Controller.
1) An architecture-aware
interference detector is invoked at each scheduling
interval to detect microarchitecture-level shared resource
interference.
2) Once such interference is detected, the architecture-aware DRM policy is used to determine VM migrations to mitigate the detected interference.

## Slide 233: More on Architecture-Aware DRM
Hui Wang, Canturk Isci, Lavanya Subramanian, Jongmoo Choi, Depei Qian, and Onur Mutlu, "A-DRM: Architecture-aware Distributed Resource Management of Virtualized Clusters" Proceedings of the 11th ACM SIGPLAN/SIGOPS International Conference on Virtual Execution Environments (VEE), Istanbul, Turkey, March 2015. [Slides (pptx) (pdf)]

## Slide 234: Interference-Aware Thread Scheduling
Advantages
  + Can eliminate/minimize interference by scheduling “symbiotic applications” together (as opposed to just managing the interference)
  + Less intrusive to hardware (less need to modify the hardware resources)
Disadvantages and Limitations
  -- High overhead to migrate threads and data between cores and machines
  -- Does not work (well) if all threads are similar and they interfere

## Slide 235: Summary

## Slide 236: Summary: Fundamental Interference Control Techniques
Goal: to reduce/control interference
1. Prioritization or request scheduling
2. Data mapping to banks/channels/ranks
3. Core/source throttling
4. Application/thread scheduling
Best is to combine all. How would you do that?

## Slide 237: Summary: Memory QoS Approaches and Techniques
Approaches: Smart vs. dumb resources
  Smart resources: QoS-aware memory scheduling
  Dumb resources: Source throttling; channel partitioning
  Both approaches are effective in reducing interference
  No single best approach for all workloads
Techniques: Request/thread scheduling, source throttling, memory partitioning
  All approaches are effective in reducing interference
  Can be applied at different levels: hardware vs. software
  No single best technique for all workloads
Combined approaches and techniques are the most powerful
  Integrated Memory Channel Partitioning and Scheduling [MICRO’11]
MCP Micro 2011 Talk

## Slide 238: Summary: Memory Interference and QoS
QoS-unaware memory 
uncontrollable and unpredictable system
Providing QoS awareness improves performance, predictability, fairness, and utilization of the memory system
Discussed many new techniques to:
  Minimize memory interference
  Provide predictable performance
Many new research ideas needed for integrated techniques and closing the interaction with software

## Slide 239: What Did We Not Cover?
Prefetch-aware shared resource management
DRAM-controller co-design
Cache interference management
Interconnect interference management
Write-read scheduling
DRAM designs to reduce interference
Interference issues in near-memory processing
…

## Slide 240: What the Future May Bring
Simple yet powerful interference control and scheduling mechanisms
  memory scheduling + interconnect scheduling
Real implementations and investigations
  SoftMC infrastructure, FPGA-based implementations
Interference and QoS in the presence of even more heterogeneity
  PIM, accelerators, …

## Slide 241: SoftMC: Open Source DRAM Infrastructure
Hasan Hassan et al., “SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies,” HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 242: SoftMC
https://github.com/CMU-SAFARI/SoftMC

## Slide 243: Some Other Ideas …

## Slide 244: Decoupled DMA w/ Dual-Port DRAM [PACT 2015]

## Slide 245: Isolating CPU and IO Traffic by Leveraging a Dual-Data-Port DRAM
Donghyuk Lee
Lavanya Subramanian, Rachata Ausavarungnirun, Jongmoo Choi, Onur Mutlu
Decoupled Direct Memory Access

## Slide 246
processor
Logical System Organization
main memory
IO devices
CPU access
IO access
Main memory connects processor and IO devices as an intermediate layer
Notes: In logical organization, system consists of processor, main memory and IO devices.
Processor accesses main memory to get data for executing instructions, called CPU access.
IO devices transfer data to main memory, called IO access.
Therefore, the main memory connects processor and IO devices as an intermediate layer.

## Slide 247
processor
Physical System Implementation
main memory
IO devices
CPU access
IO access
IO access
High Pin Cost
in Processor
High Contention
in Memory Channel
Notes: In physical implementation, however, IO devices are connected to processor,
and DMA in the processor manages the IO traffic through memory channel.
This difference between logical and physical organization leads to
High contention in memory channel,
High pin count in processor chip.

## Slide 248
processor
Our Approach
main memory
IO devices
CPU access
Enabling IO channel, decoupled & isolated from CPU channel
IO access
IO access
Notes: To avoid these problems, our approach is providing a direct connection between IO devices and main memory, which enables IO access without interfering CPU access.
We call this new memory system architecture – Decouple Direct Memory Access

## Slide 249
Executive Summary
Problem
  CPU and IO accesses contend for the shared memory channel
Our Approach: Decoupled Direct Memory Access (DDMA)
  Design new DRAM architecture with two independent data ports
   Dual-Data-Port DRAM
  Connect one port to CPU and the other port to IO devices
   Decouple CPU and IO accesses
Application
  Communication between compute units (e.g., CPU – GPU)
  In-memory communication (e.g., bulk in-memory copy/init.)
  Memory-storage communication (e.g., page fault, IO prefetch)
Result
  Significant performance improvement (20% in 2 ch. & 2 rank system)
  CPU pin count reduction (4.5%)
Notes: This is the summary of today’s talk.
The problem is that CPU and IO accesses contend for memory channel.
To mitigate this problem, we design new DRAM which has two independent data port, called dual-data-port DRAM.
We connect one port to CPU and the other port to IO devices, thereby isolating CPU and IO traffic.
We call this Decoupled Direct Memory Access (DDMA).
We can use this new memory system for
Communication between compute units,
In-memory communication, and
Memory-storage communication.
We evaluate our DDMA-based memory system and show that it provides significant performance improvement with reduction in CPU pin count.

## Slide 250
Outline
1. Problem
3. Dual-Data-Port DRAM
5. Evaluation
4. Applications for DDMA
2. Our Approach
1. Problem
Notes: This is the outline of today’s talk.
We first describe more details of the problem in conventional memory system.
Then we provide the overview of our proposed memory system.
Then we introduce one of major component, dual-data-port DRAM.
We explain how we can leverage our new memory system.
We, then, provide our evaluation methodology and results.

## Slide 251
main memory
CPU
DMA
graphics
network
storage
USB
IO interface
memory controller
Memory Channel Contention
DRAM
Chip
Processor
Chip
Problem 1: Memory Channel Contention
DMA
IO interface
Notes: This is more detailed view of a system.
CPU is connected to main memory over memory channel and
the memory controller manages accesses to the main memory.
IO devices are connected the CPU over IO interface in CPU chip.
Direct memory access unit (DMA) controls the IO traffic.
When there is a request for data in IO devices,
the requested data is first transferred to the main memory over both IO interface and the memory channel.
Then CPU accesses the main memory again to bring the requested data.
When there is a request for data in main memory,
the requested data is also transferred over the main memory.
In today’s multi-core system, all these data transfer can be happen concurrently, leading to memory channel contention.

## Slide 252
Chart: 
| CORR | SYR2K | GRAMSCHM | COVAR | SYRK | FDTD2D | 2MM | 3MM | GEMM | MVT | GESUMMV | BICG | ATAX | 3DCONV | 2DCONV
Time Spent on CPU-GPU Communication | 0.00056984 | 0.00095816 | 0.0015094 | 0.0018979 | 0.0060775 | 0.015924 | 0.027459 | 0.078553 | 0.10453 | 0.38899 | 0.39085 | 0.39323 | 0.3986 | 0.89039 | 0.91692
33.5%
on average
Fraction of Execution Time
A large fraction of the execution time is spent on IO accesses
Problem 1: Memory Channel Contention
Notes: To see the potential memory channel contention, we observe the IO traffic in GPGPU workloads.
X-axis shows the GPGPU workloads.
Y-axis shows the fraction of execution time that consume for IO accesses.
As we can see, some of GPGPU workloads mostly consumes for its execution time for computation,
however, many workloads spent significant fraction of the total execution time for transferring data between CPU and GPU. For example 33.5% on average of 8 GPGPU workloads.
Therefore, there is high demand of IO bandwidth, leading to high memory channel contention.

## Slide 253
Integrating IO interface on the processor chip leads to high area cost
Chart: 
| Others | IO Interface | Memory Channel | Power
Pin Count | 98 | 117 | 288 | 600
Chart: 
| Others | IO Interface | Memory Channel
Pin Count | 98 | 117 | 288
Processor Pin Count
(w/o power pins)
power
memory
(2 ch)
IO interface
(10.6%)
others
IO interface
(28.4%)
others
memory
(2 ch)
(w/ power pins)
Processor Pin Count
959 pins in total
359 pins in total
Problem 2: High Cost for IO Interfaces
Notes: Second problem is high area cost for IO interfaces in processor chip.
The chart shows the processor pin count of an Intel i7 processor.
As we can see, 10.6% of total pins are used for IO interfaces.
In the right chart, without counting power pints,
we see that about 19.5% of total pins are used for IO interfaces.
Therefore, integrating IO interface on processor chip leads to high processor pin count, potentially large processor chip area.

## Slide 254
Shared Memory Channel
Memory channel contention for IO access and CPU access
High area cost for integrating IO interfaces on processor chip
Notes: In summary,
IO and CPU accesses contend for memory channel.
Integrating more IO interfaces for higher bandwidth leads to high area cost on processor chip.

## Slide 255
Outline
1. Problem
3. Dual-Data-Port DRAM
5. Evaluation
4. Applications for DDMA
2. Our Approach
Notes: This is the outline of today’s talk.
We first describe more details of the problem in conventional memory system.
Then we provide the overview of our proposed memory system.
Then we introduce one of major component, dual-data-port DRAM.
We explain how we can leverage our new memory system.
We, then, provide our evaluation methodology and results.

## Slide 256
Our Approach
CPU
DMA
graphics
network
storage
USB
DRAM
Chip
main memory
?
DMA
CTRL.
DMA control
Processor
Chip
control channel
Dual-Data-
Port DRAM
Port 1
Port 2
memory controller
IO interface
DMA
Chip
DMA IO interface
Notes: As explained, our approach is directly connecting IO devices to main memory.
To this end, we first migrate IO interfaces and fraction of DMA unit out of processor chip,
we call this chip DMA IO.
DMA control unit is still existing within the processor chip, which manages off-chip DMA-IO.
To connect this off-chip DMA-IO to the main memory,
we devise a new DRAM architecture, Dual-Data-Port DRAM, which has two independent data ports,
both of which are managed by memory controller.

## Slide 257
Our Approach
?
CPU
graphics
network
storage
USB
DRAM
Chip
DMA
CTRL.
DMA control
Processor
Chip
control channel
Dual-Data-
Port DRAM
Port 1
Port 2
memory controller
DMA
Chip
DMA IO interface
IO ACCESS
Decoupled Direct Memory Access
CPU ACCESS
Notes: As explained, our approach is directly connecting IO devices to main memory.
To this end, we first migrate IO interfaces and fraction of DMA unit out of processor chip,
we call this chip DMA IO.
DMA control unit is still existing within the processor chip, which manages off-chip DMA-IO.
To connect this off-chip DMA-IO to the main memory,
we devise a new DRAM architecture, Dual-Data-Port DRAM, which has two independent data ports,
both of which are managed by memory controller.

## Slide 258
Outline
1. Problem
3. Dual-Data-Port DRAM
5. Evaluation
4. Applications for DDMA
2. Our Approach
Notes: This is the outline of today’s talk.
We first describe more details of the problem in conventional memory system.
Then we provide the overview of our proposed memory system.
Then we introduce one of major component, dual-data-port DRAM.
We explain how we can leverage our new memory system.
We, then, provide our evaluation methodology and results.

## Slide 259
peripherallogic
bank
Background: DRAM Operation
memory channel
data channel
control channel
control port
data port
control port
data port
bank
activate
read
bank
bank
READY
DRAM peripheral logic: i) controls banks, and ii) transfers data over memory channel
memory controller at CPU
Notes: We first explain the conventional DRAM organization and its operation.
DRAM consists of multiple banks and peripheral logic.
This DRAM chip is connected to the processor chip over memory channel.
This memory channel consists of a control channel and a data channel.
The DRAM peripheral logic connects these control and data channel to DRAM bank,
which are called control path and data path.
Accessing DRAM starts from activating a bank.
The bank are ready to be transfer data.
When receiving a read command, data is transferred over both data path and data channel.
In summary, DRAM periphery logic, control banks and transfer data over memory channel.

## Slide 260
bank
Problem: Single Data Port
periphery
Requests are served serially due to single data port
data channel
control channel
control port
data port
read
control port
data port
bank
READY
bank
READY
data port
read
Many
Banks
Single Data Port
memory controller at CPU
Notes: This figure shows the access scenario of multiple banks.
Now, both banks are ready to serve data and memory controller has requests for both banks.
When receiving a read command of a bank, the bank transfer data.
After finishing the data transfer, the memory controller issues another read commands, leading to transferring data.
Even though there are multiple banks which are ready to transfer data,
the peripheral logic only transfer data one after another.
Therefor, requests for multiple banks are served in serial due to limited peripheral logic.

## Slide 261
Problem: Single Data Port
RD
DATA
RD
DATA
Control Port
Data Port
time
RD
DATA
RD
Control Port
Data Port 1
time
DATA
Data Port 2
What about a DRAM with two data ports?
Notes: Specifically,
issuing a command takes one clock cycle in control channel.
However, transferring data takes multiple cycles in data channel, for example, 4 cycles for 8 data burst.
Therefore, peripheral logic for data traffic leads to more serialization for accessing DRAM.

## Slide 262
bank
periphery
twice the bandwidth & independent data ports with low overhead
data channel
control channel
data port 1
bank
bank
control port
to Port 1 (upper)
to Port 2 (lower)
bank
data bus
port select signal
data port 2
data channel
mux
mux
Overhead
Area: 1.6% ↑
Pins: 20 ↑
Dual-Data-Port DRAM
Notes: We add additional data data port and data path.
To manage the connections between bank and these two data port, we add a multiplexer per each bank.
The multiple makes any connection in the three nodes – bank data bus, upper data port, and lower data port.
To manage the multiplexer, we add a control signal, port select, in the control channel.
We called this new DRAM architecture, Dual-Data-Port DRAM, which has twice bandwidth and two independent data ports.

## Slide 263
DDP-DRAM Memory System
bank
periphery
CPU channel
control channel
with port select
data port 1
bank
bank
control port
data port 2
IO channel
mux
mux
DDMA IO interface
memory controller at CPU
Notes: We integrate this Dual-Data-Port DRAM in a system by connecting a data port to CPU and the other to DDM-IO.
In our architecture, Both data ports and DDMA-IO are controlled by the memory controller in the processor.

## Slide 264
Three Data Transfer Modes
CPU Access: Access through CPU channel
  DRAM read/write with CPU port selection
IO Access: Access through IO channel
  DRAM read/write with IO port selection
Port Bypass: Direct transfer between channels
  DRAM access with port bypass selection
Notes: Our Dual-Data-Port DRAM supports three access mode, CPU access, IO access, and Port Bypass.
Let us take a look at more details of these three modes.

## Slide 265
1. CPU Access Mode
bank
periphery
CPU channel
bank
control port
data port 2
IO channel
DDMA IO interface
control channel
with port select
mux
mux
data port
bank
READY
memory controller at CPU
read
control port
CPU channel
data port 1
control channel
with CPU channel
Notes: In CPU access mode, memory controller simply issues read command with CPU port selection.
Then, DRAM periphery builds the connection between bank and CPU port,
and transfer data to CPU, which is same as DRAM access in conventional systems.

## Slide 266
2. IO Access Mode
bank
periphery
CPU channel
bank
control port
IO channel
DDMA IO interface
control channel
with port select
mux
mux
data port 1
control channel
with IO channel
memory controller at CPU
IO channel
data port
data port 2
bank
READY
read
control port
Notes: In IO Access mode, memory controller issues read/write command with IO port selection.
Then, DRAM peripheral logic builds the connection between bank and IO port,
and transfer data to IO channel.
DDMA-IO, then, read data from IO channel.

## Slide 267
3. Port Bypass Mode
bank
periphery
CPU channel
bank
control port
IO channel
control channel
with port select
mux
mux
control channel
with port bypass
IO channel
bank
data port
data port
data port 2
data port 1
CPU channel
DDMA IO interface
memory controller at CPU
Notes: In Port Bypass mode, memory controller issues read/write command with both ports selection.
Then, DRAM peripheral logic builds the connection between these two ports,
then memory controller and DDMA-IO directly communicate over DRAM peripheral logic.

## Slide 268
Outline
1. Problem
3. Dual-Data-Port DRAM
5. Evaluation
4. Applications for DDMA
2. Our Approach
Notes: This is the outline of today’s talk.
We first describe more details of the problem in conventional memory system.
Then we provide the overview of our proposed memory system.
Then we introduce one of major component, dual-data-port DRAM.
We explain how we can leverage our new memory system.
We, then, provide our evaluation methodology and results.

## Slide 269
Three Applications for DDMA
Communication b/w Compute Units
  CPU-GPU communication
In-Memory Communication and Initialization
  Bulk page copy/initialization
Communication b/w Memory and Storage
  Serving page fault/file read & write
Notes: First, DDMA supports communication between compute units.
For example, CPU-GPU communication.
Second, DDMA supports In-memory communication and initialization.
For example, bulk page copy and initialization can perform through DDMA.
Third, DDMA support communication between memory and storage.
For example, page fault, file read and write.
This feature also enables aggressive IO prefetching.
Let us take a look at more details of these mechanisms.

## Slide 270
ctrl. channel
DDMA ctrl.
read
with IO sel.
CPU → GPU
1. Compute Unit ↔ Compute Unit
CPU
DDMA
ctrl.
memory controller
DDP-DRAM
DDMA IO interface
GPU
DDMA
ctrl.
memory controller
DDP-DRAM
DDMA IO interface
ctrl. channel
DDMA ctrl.
destination
DDMA IO interface
source
Ack.
destination
DDMA IO interface
write
with IO sel.
Transfer data through DDMA without interfering w/ CPU/GPU memory accesses
CPU
memory controller
GPU
memory controller
Notes: This figure shows two systems, CPU system and GPU system that has their own memory system.
The communication scenario is transferring data from CPU memory to GPU memory.
To this end,
CPU memory controller issues read commands to transfer data to CPU DDMA-IO.
Then, CPU DDMA-IO transfers data to GPU DDMA-IO.
GPU DDMA-IO lets GPU knows about the data transfer.
Then, GPU memory controller issues write commands to transfer data to DRAM.

## Slide 271
ctrl. chan.
read
with IO sel.
write
with IO sel.
2. In-Memory Communication
DDMA ctrl.
CPU
DDMA
ctrl.
memory controller
DDP-DRAM
DDMA IO interface
source
destination
Transfer data in DRAM through DDAM without interfering with CPU memory accesses
CPU
memory controller
Notes: The communication scenario is migrating data from one location to the other location within DRAM.
To this end,
The memory controller first issues read command with IO port select to transfer data to DDMA-IO.
The memory controller, then, issues write command with IO port select to transfer data to DRAM.

## Slide 272
DDMA ctrl.
Acc. Storage
Ack.
3. Memory ↔ Storage
ctrl. chan.
write
with IO sel.
CPU
DDMA
ctrl.
memory controller
DDP-DRAM
DDMA IO interface
Storage
Storage (source)
destination
DDMA IO interface
Transfer data from storage through DDMA without interfering with CPU memory accesses
destination
CPU
memory controller
Notes: The communication scenario in this figure is transferring data from storage to main memory.
To this end,
DDMA-IO first brings data from storage.
Then, DDMA-IO lets CPU know the data traffic from storage.
The memory controller, then, issues write command to transferring the data to DRAM.

## Slide 273
Outline
1. Problem
3. Dual-Data-Port DRAM
5. Evaluation
4. Applications for DDMA
2. Our Approach
Notes: This is the outline of today’s talk.
We first describe more details of the problem in conventional memory system.
Then we provide the overview of our proposed memory system.
Then we introduce one of major component, dual-data-port DRAM.
We explain how we can leverage our new memory system.
We, then, provide our evaluation methodology and results.

## Slide 274
Evaluation Methods
System
  Processor: 4 – 16 cores
  LLC: 16-way associative, 512KB private cache-slice/core
  Memory: 1 – 4 ranks and 1 – 4 channels
Workloads
  Memory intensive: SPEC CPU2006, TPC, stream (31 benchmarks)
  CPU-GPU communication intensive: polybench (8 benchmarks)
  In-memory communication intensive: apache, bootup, compiler, filecopy, mysql, fork, shell, memcached (8 in total)
Notes: We model systems that have 4 to 16 cores and memory systems that have 1 to 4 ranks and 1 to 4 channels.
We builds workloads by randomly selecting from three benchmark categories.
Memory intensive benchmark from SPEC CPU 20016, TPC, stream
CPU-GPU communication benchmarks from Polybench
In-memoy intensive benchmarks,

## Slide 275
Chart: 
| 4-Core | 8-Core | 16-Core
C2R2 | 0.079197 | 0.14666 | 0.20091
Chart: 
| 4-Core | 8-Core | 16-Core
C4R1 | 0.052178 | 0.11706 | 0.20439
Performance Improvement
Performance Improvement
CPU-GPU Comm.-Intensive
In-Memory Comm.-Intensive
More performance improvement at higher core count
High performance improvement
Performance (2 Channel, 2 Rank)
Notes: We first observe the performance improvement in 2 rank and 2 channel memory systems.
Left figure shows the case for CPU-GPU communication-intensive workloads.
X axis shows the number of cores and Y axis are weighted speedup improvement.
As we can see, our mechanism provides significant performance improvement and provide more performance improvement in more core counts. More core systems provide more inflight requests the main memory, leading to higher contention in memory channel. By decoupling IO accesses from the memory channel, our mechanism provides more performance improvement at more core systems.
We observe similar results for in-memory communication-intensive workloads.
We conclude that our mechanism provide more performance improvement for more core systems.

## Slide 276
Performance on Various Systems
Chart: 
| 1 rank | 2 rank | 4 rank
16-Core | 0.23101 | 0.27317 | 0.31961
Chart: 
| 1 ch | 2 ch | 4 ch
16-Core | 0.23101 | 0.14869 | 0.080779
Channel Count
Rank Count
Performance Improvement
Performance Improvement
Performance increases with rank count
Notes: Now we vary the memory system configuration of the number of ranks and channels.
X axis shows channel and rank count.
Y axis are weighted speedup improvement.
When increasing the number of channels, our mechanism provides less benefits in performance mainly due to the reduced memory channel conflicts in more-channel memory systems.
When increasing the number of ranks, our mechanism provides more benefits in performance mainly due to higher conflicts in more-rank memory system.
In summary, our mechanism provides more performance improvement at more memory ranks and less memory channels.

## Slide 277
Chart: 
| 1 ch | 1 ch DDMA | 2 ch
16-Core | 959 | 915 | 1103
Chart: 
| 1 ch | 1 ch DDMA | 2 ch
16-Core | 1 | 1.3226 | 1.5952
Performance
Processor Pin Count
DDMA achieves higher performance at lower processor pin count
959
915
1103
DDMA vs. Dual Channel
Notes: We compare our mechanism to the case, simply increasing channel counts.
Left figure shows performance comparison of three memory system, baseline – 1 channel memory system, our proposal – 1 channel with DDMA, and 2 channel memory system.
Our mechanism provides significant performance improvement over the baseline 1 channel memory system. but, less performance benefit than 2 channel memory system.
However, increasing channel count leads to significant increase in processor pins.
We compare this trade off in right figure. Y axis are package pin count. Adding one more memory channel requires significant additional processor pins (144 pins per channel). On the other hand, using DDMA reduces processors pins mainly due to migrated IO interfaces out of processors chip.
Therefore, our mechanism achieves higher performance at lower processor pin count.

## Slide 278: More on Decoupled DMA
Donghyuk Lee, Lavanya Subramanian, Rachata Ausavarungnirun, Jongmoo Choi, and Onur Mutlu, "Decoupled Direct Memory Access: Isolating CPU and IO Traffic by Leveraging a Dual-Data-Port DRAM" Proceedings of the 24th International Conference on Parallel Architectures and Compilation Techniques (PACT), San Francisco, CA, USA, October 2015. [Slides (pptx) (pdf)]

## Slide 279: Memory Systems Fundamentals, Recent Research, Challenges, Opportunities Lecture 6: Memory Interference and QoS
Prof. Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
10 October 2018
Technion Fast Course 2018

## Slide 280: Interconnect QoS/Performance Ideas

## Slide 281: Application-Aware Prioritization in NoCs
Das et al., “Application-Aware Prioritization Mechanisms for On-Chip Networks,” MICRO 2009.
  https://users.ece.cmu.edu/~omutlu/pub/app-aware-noc_micro09.pdf

## Slide 282: Slack-Based Packet Scheduling
Reetuparna Das, Onur Mutlu, Thomas Moscibroda, and Chita R. Das, "Aergia: Exploiting Packet Latency Slack in On-Chip Networks" Proceedings of the 37th International Symposium on Computer Architecture (ISCA), pages 106-116, Saint-Malo, France, June 2010. Slides (pptx)

## Slide 283: Low-Cost QoS in On-Chip Networks (I)
Boris Grot, Stephen W. Keckler, and Onur Mutlu, "Preemptive Virtual Clock: A Flexible, Efficient, and Cost-effective QOS Scheme for Networks-on-Chip" Proceedings of the 42nd International Symposium on Microarchitecture (MICRO), pages 268-279, New York, NY, December 2009. Slides (pdf)

## Slide 284: Low-Cost QoS in On-Chip Networks (II)
Boris Grot, Joel Hestness, Stephen W. Keckler, and Onur Mutlu, "Kilo-NOC: A Heterogeneous Network-on-Chip Architecture for Scalability and Service Guarantees" Proceedings of the 38th International Symposium on Computer Architecture (ISCA), San Jose, CA, June 2011. Slides (pptx)

## Slide 285: Throttling Based Fairness in NoCs
Kevin Chang, Rachata Ausavarungnirun, Chris Fallin, and Onur Mutlu, "HAT: Heterogeneous Adaptive Throttling for On-Chip Networks" Proceedings of the 24th International Symposium on Computer Architecture and High Performance Computing (SBAC-PAD), New York, NY, October 2012. Slides (pptx) (pdf)

## Slide 286: Scalability: Express Cube Topologies
Boris Grot, Joel Hestness, Stephen W. Keckler, and Onur Mutlu, "Express Cube Topologies for On-Chip Interconnects" Proceedings of the 15th International Symposium on High-Performance Computer Architecture (HPCA), pages 163-174, Raleigh, NC, February 2009. Slides (ppt)

## Slide 287: Scalability: Slim NoC
Maciej Besta, Syed Minhaj Hassan, Sudhakar Yalamanchili, Rachata Ausavarungnirun, Onur Mutlu, Torsten Hoefler, "Slim NoC: A Low-Diameter On-Chip Network Topology for High Energy Efficiency and Scalability" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pdf)]

## Slide 288: Bufferless Routing in NoCs
Moscibroda and Mutlu, “A Case for Bufferless Routing in On-Chip Networks,” ISCA 2009.
  https://users.ece.cmu.edu/~omutlu/pub/bless_isca09.pdf

## Slide 289: CHIPPER: Low-Complexity Bufferless
Chris Fallin, Chris Craik, and Onur Mutlu, "CHIPPER: A Low-Complexity Bufferless Deflection Router" Proceedings of the 17th International Symposium on High-Performance Computer Architecture (HPCA), pages 144-155, San Antonio, TX, February 2011. Slides (pptx) An extended version as SAFARI Technical Report, TR-SAFARI-2010-001, Carnegie Mellon University, December 2010.

## Slide 290: Minimally-Buffered Deflection Routing
Chris Fallin, Greg Nazario, Xiangyao Yu, Kevin Chang, Rachata Ausavarungnirun, and Onur Mutlu, "MinBD: Minimally-Buffered Deflection Routing for Energy-Efficient Interconnect" Proceedings of the 6th ACM/IEEE International Symposium on Networks on Chip (NOCS), Lyngby, Denmark, May 2012. Slides (pptx) (pdf)

## Slide 291: “Bufferless” Hierarchical Rings
Ausavarungnirun et al., “Design and Evaluation of Hierarchical Rings with Deflection Routing,” SBAC-PAD 2014.
  http://users.ece.cmu.edu/~omutlu/pub/hierarchical-rings-with-deflection_sbacpad14.pdf
Discusses the design and implementation of a mostly-bufferless hierarchical ring

## Slide 292: “Bufferless” Hierarchical Rings (II)
Rachata Ausavarungnirun, Chris Fallin, Xiangyao Yu, Kevin Chang, Greg Nazario, Reetuparna Das, Gabriel Loh, and Onur Mutlu, "A Case for Hierarchical Rings with Deflection Routing: An Energy-Efficient On-Chip Communication Substrate" Parallel Computing (PARCO), to appear in 2016.
  arXiv.org version, February 2016.

## Slide 293: Summary of Six Years of Research
Chris Fallin, Greg Nazario, Xiangyao Yu, Kevin Chang, Rachata Ausavarungnirun, and Onur Mutlu, "Bufferless and Minimally-Buffered Deflection Routing" Invited Book Chapter in Routing Algorithms in Networks-on-Chip, pp. 241-275, Springer, 2014.

## Slide 294: On-Chip vs. Off-Chip Tradeoffs
George Nychis, Chris Fallin, Thomas Moscibroda, Onur Mutlu, and Srinivasan Seshan, "On-Chip Networks from a Networking Perspective: Congestion and Scalability in Many-core Interconnects" Proceedings of the 2012 ACM SIGCOMM Conference (SIGCOMM), Helsinki, Finland, August 2012. Slides (pptx)

## Slide 295: Slowdown Estimation in NoCs
Xiyue Xiang, Saugata Ghose, Onur Mutlu, and Nian-Feng Tzeng, "A Model for Application Slowdown Estimation in On-Chip Networks and Its Use for Improving System Fairness and Performance" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016. [Slides (pptx) (pdf)]

## Slide 296: Handling Multicast and Hotspot Issues
Xiyue Xiang, Wentao Shi, Saugata Ghose, Lu Peng, Onur Mutlu, and Nian-Feng Tzeng, "Carpool: A Bufferless On-Chip Network Supporting Adaptive Multicast and Hotspot Alleviation" Proceedings of the International Conference on Supercomputing (ICS), Chicago, IL, USA, June 2017. [Slides (pptx) (pdf)]

## Slide 297: Predictable Performance Again: Strong Memory Service Guarantees

## Slide 298: Remember MISE?
Lavanya Subramanian, Vivek Seshadri, Yoongu Kim, Ben Jaiyen, and Onur Mutlu, "MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA), Shenzhen, China, February 2013. Slides (pptx)

## Slide 299: Extending Slowdown Estimation to Caches
How do we extend the MISE model to include shared cache interference?
Answer: Application Slowdown Model
Lavanya Subramanian, Vivek Seshadri, Arnab Ghosh, Samira Khan, and Onur Mutlu, "The Application Slowdown Model: Quantifying and Controlling the Impact of Inter-Application Interference at Shared Caches and Main Memory" Proceedings of the 48th International Symposium on Microarchitecture (MICRO), Waikiki, Hawaii, USA, December 2015. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Source Code]

## Slide 300: Quantifying and Controlling Impact of Interference at Shared Caches and Main Memory
Lavanya Subramanian, Vivek Seshadri,
Arnab Ghosh, Samira Khan, Onur Mutlu
Application Slowdown Model

## Slide 301: Shared Cache and Memory Contention
Main Memory
Shared
Cache
Capacity
Core
Core
Core
Core
MISE [HPCA’13]

## Slide 302: Cache Capacity Contention
Main Memory
Shared
Cache
Cache
Access Rate
Priority
Core
Core
Applications evict each other’s blocks
from the shared cache

## Slide 303: Estimating Cache and Memory Slowdowns
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Main Memory
Shared
Cache
Cache
Service Rate
Memory Service Rate

## Slide 304: Service Rates vs. Access Rates
Request service and access rates
are tightly coupled
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Main Memory
Shared
Cache
Cache
Service Rate
Cache Access Rate

## Slide 305: The Application Slowdown Model
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Main Memory
Shared
Cache
Cache Access Rate

## Slide 306: Real System Studies: Cache Access Rate vs. Slowdown
Chart: Cache Access Rate Ratio
| 1.956639859309423 | 1.4244011693845899 | 1.2634952603669141 | 1.2398817773717179 | 1.2327504382395451 | 1.1866685232301459 | 1.1281807279586351 | 1.124058161263338 | 1.0852248306002079 | 1.049730923564083 | 1.0308963402118509 | 1
astar | 2.0976 | 1.4098 | 1.2836 | 1.2286 | 1.2286 | 1.1781 | 1.1316 | 1.0886 | 1.075 | 1.0238 | 1.0118 | 1
lbm | 1.9524 | 1.5769 | 1.268 | 1.2178 | 1.1714 | 1.1604 | 1.0982 | 1
bzip2 | 1.5672 | 1.448 | 1.3189 | 1.2404 | 1.11 | 1

## Slide 307: Challenge
How to estimate alone cache access rate?
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Main Memory
Shared
Cache
Cache
Access Rate
Auxiliary Tag Store
Priority

## Slide 308: Auxiliary Tag Store
Main Memory
Shared
Cache
Cache
Access Rate
Auxiliary Tag Store
Priority
Core
Core
Still in auxiliary tag store
Auxiliary Tag Store
Auxiliary tag store tracks such contention misses

## Slide 309: Accounting for Contention Misses
Revisiting alone memory request service rate
Cycles serving contention misses should not
count as high priority cycles

## Slide 310: Alone Cache Access Rate Estimation
Cache Contention Cycles: Cycles spent serving contention misses
From auxiliary tag store
when given high priority
Measured when given high priority

## Slide 311: Application Slowdown Model (ASM)
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Main Memory
Shared
Cache
Cache
Access Rate

## Slide 312: Previous Work on Slowdown Estimation
Previous work on slowdown estimation
  STFM (Stall Time Fair Memory) Scheduling [Mutlu et al., MICRO ’07]
  FST (Fairness via Source Throttling) [Ebrahimi et al., ASPLOS ’10]
  Per-thread Cycle Accounting [Du Bois et al., HiPEAC ’13]
Basic Idea:
Count interference experienced by each request  Difficult
ASM’s estimates are much more coarse grained  Easier
Notes: The most relevant previous works on slowdown estimation are STFM, stall time fair memory scheduling and FST, fairness via source throttling.
FST employs similar mechanisms as STFM for memory-induced slowdown estimation, therefore, I will focus on STFM for the rest of the evaluation.
STFM estimates slowdown as the ratio of alone to shared stall times.
Stall time shared is easy to measure, analogous to shared request service rate
Stall time alone is harder and STFM estimates it by counting the number of cycles an application receives interference from other applications.

## Slide 313: Model Accuracy Results
Average error of ASM’s slowdown estimates: 10%
Select applications
Chart: Slowdown Estimation Error (in %)
| calculix | povray | tonto | namd | dealII | sjeng | perlbench | gobmk | xalancbmk | sphinx3 | GemsFDTD | omnetpp | lbm | leslie3d | soplex | milc | libq | mcf | NPBbt | NPBft | NPBis | NPBua | Average
FST | 0.41045 | 2.0079 | 5.1953 | 1.8752 | 31.7637 | 3.9164 | 5.0801 | 5.7555 | 10.2045 | 28.8548 | 53.2408 | 33.9099 | 85.5316 | 23.7095 | 78.2879 | 28.8525 | 21.6335 | 144.5315 | 0 | 29.7229 | 45.8772 | 32.1654 | 29.737 | 0 | 29.3729
PTCA | 1.9106 | 3.68 | 7.5351 | 4.5745 | 32.2882 | 10.317 | 35.1831 | 16.1571 | 27.705 | 6.4247 | 32.3625 | 22.1458 | 33.7427 | 19.2084 | 81.8627 | 11.1493 | 104.3351 | 108.3397 | 0 | 3.1958 | 133.656 | 9.1995 | 69.8224 | 0 | 40.3875
ASM | 11.8215 | 1.6467 | 5.8829 | 3.6925 | 9.8046 | 7.3422 | 10.7283 | 6.569 | 6.5517 | 7.5311 | 11.4907 | 12.3207 | 13.0691 | 5.7255 | 9.5044 | 8.1542 | 2.8033 | 23.1982 | 0 | 2.5694 | 14.7302 | 7.6906 | 4.199 | 0 | 9.8567

## Slide 314: Leveraging ASM’s Slowdown Estimates
Slowdown-aware resource allocation for high performance and fairness
Slowdown-aware resource allocation to bound application slowdowns
VM migration and admission control schemes
[VEE ’15]
Fair billing schemes in a commodity cloud

## Slide 315: Cache Capacity Partitioning
Main Memory
Shared
Cache
Cache
Access Rate
Core
Core
Goal: Partition the shared cache among applications to mitigate contention

## Slide 316: Cache Capacity Partitioning
Main Memory
Core
Core
Way
2
Set 0
Set 1
Set 2
Set 3
..
Set N-1
Way
0
Way
1
Way
3
Previous partitioning schemes optimize for miss count
Problem: Not aware of performance and slowdowns

## Slide 317: ASM-Cache: Slowdown-aware Cache Way Partitioning
Key Requirement: Slowdown estimates for all possible way partitions
Extend ASM to estimate slowdown for all possible cache way allocations
Key Idea: Allocate each way to the application whose slowdown reduces the most

## Slide 318: Memory Bandwidth Partitioning
Main Memory
Shared
Cache
Cache
Access Rate
Core
Core
Goal: Partition the main memory bandwidth among applications to mitigate contention

## Slide 319: ASM-Mem: Slowdown-aware Memory Bandwidth Partitioning
Key Idea: Allocate high priority proportional to an application’s slowdown
Application i’s requests given highest priority at the memory controller for its fraction

## Slide 320: Coordinated Resource Allocation Schemes
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Main Memory
Shared
Cache
Cache capacity-aware
bandwidth allocation
1. Employ ASM-Cache to partition cache capacity
2. Drive ASM-Mem with slowdowns from ASM-Cache

## Slide 321: Fairness and Performance Results
16-core system 100 workloads
Significant fairness benefits across different channel counts
Chart: Number of Channels
FRFCFS-NoPart | 10.498 | 6.9257
FRFCFS+UCP | 9.4748 | 6.0393
TCM+UCP | 10.4292 | 6.592
PARBS+UCP | 9.3348 | 6.033
ASM-Cache-Mem | 7.9617 | 5.5061
Chart: Number of Channels
FRFCFS-NoPart | 0.212 | 0.30811
FRFCFS+UCP | 0.20694 | 0.30879
TCM+UCP | 0.19336 | 0.28617
PARBS+UCP | 0.21259 | 0.31157
ASM-Cache-Mem | 0.20928 | 0.30633

## Slide 322: Summary
Problem: Uncontrolled memory interference cause high and unpredictable application slowdowns
Goal: Quantify and control slowdowns
Key Contribution:
  ASM: An accurate slowdown estimation model
  Average error of ASM: 10%
Key Ideas:
  Shared cache access rate is a proxy for performance
  Cache Access Rate Alone can be estimated by minimizing memory interference and quantifying cache interference
Applications of Our Model
  Slowdown-aware cache and memory management to achieve high performance, fairness and performance guarantees
Source Code Released in January 2016

## Slide 323: More on Application Slowdown Model
Lavanya Subramanian, Vivek Seshadri, Arnab Ghosh, Samira Khan, and Onur Mutlu, "The Application Slowdown Model: Quantifying and Controlling the Impact of Inter-Application Interference at Shared Caches and Main Memory" Proceedings of the 48th International Symposium on Microarchitecture (MICRO), Waikiki, Hawaii, USA, December 2015. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Source Code]